## Slide 1: And the Name …

## Slide 2
ByteFrost

## Slide 3: ByteFrost Addressing Modes
Immediate
General Register
Address Register
Memory
There are four forms of memory in the ByteFrost – Immediates (read-only), General-Purpose Registers (R0 – R3), Address Registers (DP, SP, PC), and Memory (64KB divided into ROM, RAM, and MMIO regions)
Every solid directed edge (u, v) in the following graph means that memory u can write to memory v with a dedicated instruction.
Every dotted directed edge (u, v) means that the memory u can write to memory v indirectly (i.e., a path exists from u to v but requires multiple instructions to implement).
There are technically 4 x 4 = 16 possible permutations here, but as immediates are read-only, there are in effect only 3 x 4 = 12 possible permutations.
Instructions with an asterisk (*) are currently not implemented.
Dest | Src | Dedicated Instruction? | Form(s)
GR | Imm | Yes (LDR) | Rd = Imm_8 (LDR Rd, Imm)
GR | GR | Yes (MOV) | Rd = Rs (MOV Rd, Rs)
GR | AR | Yes (MVA*) | Rd = AR[i][L/H] (MVA Rd, %L/RAR)
GR | Memory | Yes (LMA, LMR, LMO*) | (LMA) Rd = *{%HDP, Imm} (LMR) Rd = *{%HDP, Rs} (LMO) Rd = *(AR[i] + Imm)
Dest | Src | Form
GR | Imm | 
GR | GR | 
GR | AR | 
GR | Memory | 
Dest | Src | Form
GR | Imm | 
GR | GR | 
GR | AR | 
GR | Memory | 
LDR
MOV
MVA*
LMA, LMR, LMO*

## Slide 4: ByteFrost V2.0 – 16bit Address

## Slide 5: Unified Bus Operation (v2.0)
3msb
CE
CE
Data Bus
Data Bus
Data Bus
Instruction Registers
SRAM
EEPROM
Address Bus + Read/Write
Stack Pointer
Program Counter
AMAP
Decoder
MMIO
Micro
Instructions
Read /Write
Register
File
Addr H
Addr L
Base Pointer
TmpAR
16bitAdder
8b16b
AR Select
CE
8 lsb
8 msb
Data Pointer
PC
SP
DP
BP
TmpAR

## Slide 6: ByteFrost Addressing Modes
Immediate
General Register
Address Register
Memory
There are five forms of memory in the ByteFrost – Immediates (read-only), General-Purpose Registers (R0 – R3), Address Registers (DP, SP, PC, BP), Memory (64KB divided into ROM, RAM, and MMIO regions), and Stack
Every solid directed edge (u, v) in the following graph means that memory u can write to memory v with a dedicated instruction.
Every dotted directed edge (u, v) means that the memory u can write to memory v indirectly (i.e., a path exists from u to v but requires multiple instructions to implement).
There are technically 5 x 5 = 25 possible permutations here, but as immediates are read-only, there are in effect only 5 x 4 = 20 possible permutations.
Instructions with an asterisk (*) are currently not implemented.
Src | Dest | Semantics | Dedicated Instruction?
Imm | GR | Rd = Imm_8 (LDR Rd, Imm) | Yes (LDR)
GR | GR | Rd = Rs (MOV Rd, Rs) | Yes (MOV)
AR | GR | Rd = ARSrc[L/H] | Yes (*)
Memory | GR | (LMA) Rd = *{%DP[H], Imm}, DP[L] = Imm (LMR) Rd = *{%DP[H], Rs}, DP[L] = Rs (LMO*) Rd = *(ARSrc + Imm) | Yes (LMA, LMR, *
Stack | GR | Rd = *(SP), SP++ | Yes (POP)
Stack
LDR
MOV
Src | Dest | Semantics | Dedicated Instruction?
Imm | AR | ARDest[L/H] = Imm | Yes (*)
GR | AR | ARDest[L/H] = Rs | Yes (*)
AR | AR | ARDest = ARSrc + Imm | Yes (*)
Memory | AR | ARDest[L/H] = *(ARSrc + Imm) (?) ARDest = *{ARSrc + Imm + 1, ARSrc + Imm} (?) | No
Stack | AR | ARDest = *{SP + 1, SP}, SP += 2 (?) (e.g. POP ARDest) | No
Src | Dest | Semantics | Dedicated Instruction?
Imm | Memory | *(ARSrc) = Imm (?) | No
GR | Memory | *(ARSrc + Imm) = Rs | Yes (*)
AR | Memory | *(ARDest + Imm + 1, ARDest + Imm) = ARSrc(?) | No
Memory | Memory | *(ARDest + Imm) = *(ARSrc) | No (load-store architecture)
Stack | Memory | *(ARSrc + Imm) = *SP, SP++ (?) | No
Src | Dest | Semantics | Dedicated Instruction?
Imm | Stack | *(SP) = Imm, SP– (Push Imm) | No?
GR | Stack | *(SP) = Rs, SP-- | Yes (PUSH *) (change to full-descending)
AR | Stack | *(SP, SP – 1) = ARSrc, SP -= 2 | No? (Push ARSrc)
Memory | Stack | ? | ?
Stack | Stack | ? | ?

## Slide 7: Address Bus Arbiter (v2.0)
138: Addr Bus Arbiter
µC 14: SP Addr
FetchCycle
Data Pointer OE
Stack Pointer OE
Program Counter OE
Bus Grant
When the bus is granted to MMIO Master (SD Card) all other masters set to three state (No one transmit address on the bus)
Note: The Address Bus Arbiter Deprecated. It is replaced by the ARSelect LUT.
Remove

## Slide 8: Address Bus Select (ARSelect) v2.0
ARSelect 8x8 LUT
Inputs |  |  |  |  |  |  | Outputs (Active Low)
Bus Grant (A7) | Fetch Cycle (A6) | PC Out control signal (A5) | SP Out control signal (A4) | TmpAR Write control signal (A3) | Opcode_MAG_LDW_SDW_MAA (Active Low) (A2) | AR Src operand (A1, A0) | 
1 | X | X | X | X | X | X | None (Bus floats)
0 | 1 | X | X | X | X | X | PC (I/O 0)
0 | 0 | 1 | X | X | X | X | PC (I/O 0)
0 | 0 | 0 | 1 | X | X | X | SP (I/O 2)
0 | 0 | 0 | 0 | 1 | X | X | TmpAR (I/O 4)
0 | 0 | 0 | 0 | 0 | MAG, LDW, SDW, MAA | AR Src[1:0] | = AR Src[1:0] 0-PC, 1-DP, 2-SP, 3-BP
0 | 0 | 0 | 0 | 0 | Other Opcodes | X | DP (I/O 0)
ARSelect specifies which AR gets to write to the Address Bus and whether any of them do (it can do this since it only sends output enables; if it doesn’t send an output enable to any hardware entity, then no entity writes to the address bus).
EEPROM Data Output Bit | Output
7 | 1 (unused)
6 | 1 (unused)
5 | 1 (unused)
4 | TmpAR Output Enable (ACTIVE LOW)
3 | BP Output Enable (ACTIVE LOW)
2 | SP Output Enable (ACTIVE LOW)
1 | DP Output Enable (ACTIVE LOW)
0 | PC Output Enable (ACTIVE LOW)
Bus Grant
FetchCycle
Program Counter OE
µC 9: PC Out
µC 14: SP Out
Stack Pointer OE
µC 20: TmpARWrite
Opcode_MAG_LDW_SDW_MAA
ARSrc [1:0]
Data Pointer OE
TmpAR OE
Temporary dangled

## Slide 9: Opcode_MAG_LDW_SDW_MAA (v2.0)
74LS30
LDWL
OpCode_14
LDWH
OpCode_15
SDWL
OpCode_16
SDWH
OpCode_17
MAAL
OpCode_18
MAAH
OpCode_19
MAG
OpCode_1A
Opcode_MAA
OpCode_10
JSR
Opcode_MAA_JSR
Opcode_MAG_LDW_SDW_MAA

## Slide 10: ARSrc Operand Decode v2.0
ARSrc [1:0]
157: ARSrc
Instr[5],Instr[1]
ARSrc Decode:
If opcode is of (AR  GR) (Rd = ARSrc[L/H]) instruction, then ARSrc is in bits 9:8.
Otherwise, ARSrc is a function of bits 5 and the opcode (maybe the opcode’ least significant bit?)
Instructions that specify ARSrc with 1 bit in bit 5 need to get the other bit from the opcode; if we always assign these two-opcode instructions opcodes as [4-bit opcode x][0/1], then we can get the other ARSrc bit from the least significant bit of the opcode, i.e., in these instructions ARSrc is {Instr[5], Instr[0]} (in bits 5 and 0)
Instr[9],Instr[8]
Instr[9],Instr[8]
Instr[5],Instr[1]
0v
OpCode_MAG

## Slide 11: Address to Data Bus
574: Addr Hi
574: Addr Lo
Address Bus
Data
[7:0]
Data
[7:0]
Main CLK
Addr Hi
[15:8]
Addr Hi
[15:8]
Data Bus
CD4053 A
0
1
CD4053 B
0
1
CD4053 C
0
1
µC 22: AB2DB H/L
µC 21: AB2DB
1
1
Opcode_MAA_JSR
AR H/L (Instr[5])
0v
0v
0v
5v
Opcode_MAA_JSR
µC 22: AB2DB H/L
AR H/L (Instr[5])
0v
0v
Addr Hi OE
Addr Lo OE
µC 21: AB2DB
µC 21: AB2DB
Addr Hi OE
Addr Lo OE

## Slide 12: TmpAR (Address Offset Adder) v2.0
Addr Lo
[7:0]
TmpAR OE
574: TmpAR Hi
574: TmpAR Lo
Address Bus
Addr Low
[7:0]
Addr Hi
[15:8]
Main CLK
283: Add 3:0
283: Add 3:0
283: Add 3:0
283: Add 3:0
Addr Hi
[15:8]
Addr Hi
[15:8]
Address Bus
Data Bus
Addr Hi
[15:8]
Data
Sign Extended
[15:8]
Data
[7:0]
The only control in this circuit is the TmpAR OE which
Writes to the Address bus the sum of
Address+Data from last clock

## Slide 13: Address Map Decoder (v2.0)
0000 – 1FFF | ROM
2000 – 3FFF | RAM
4000 – 5FFF | 
6000 – 7FFF | 
8000 – 9FFF | 
A000 – BFFF | 
C000 – DFFF | 
E000 – FFFF | MMIO
138 AMAP
138 AMAP
~SRAM Chip En
74HC21
74HC21
~EEPROM Chip En
Address Bus + Read/Write
A15..A13
138 MMIO Device Enable
A12
A11
A10
A9
~SD Card Device En
MMIO
E000 – E1FF | SD Card
E200 – E3FF | Counter
E400 – E5FF | 
E600 – E7FF | 
E800 – E9FF | 
EA00 – EBFF | 
EC00 – EDFF | 
EE00 – EFFF | 
F000 – FFFF | No HW
Address Map
~Counter Device En

## Slide 14: Memory Access (v2.0)
Cycle | Signal | SRAM | EEPROM | MMIO
Memory Write | #WE | #WE | ‘1’ (no writes) | #WE
Memory Read | #OE | #OE |  | 
Memory Write or Memory Read | #CE | (~SRAM Chip En) | (~EEPROM Chip En) | MMIO
µC 10: MEM Read
FetchCycle
#OE
Main CLK
µC 11: MEM Write
#WE

## Slide 15: SRAM (v2.0)
Data
Bus
I/O[0:7]
SRAM
A0..A15
15
Address Bus + Read/Write
~SRAM Chip En
#OE
#WE

## Slide 16: EEPROM (v2.0)
Data Bus
Prog EEPROM
Addr
[15:0]
Prog
Data[7:0]
16
Address Bus
~EEPROM Chip En
#OE

## Slide 17: Load Special Pointer (LSP) (v2.0)
Main CLK
138: LSP
µC 17: LSP
OpCode
[7:6] SP
Ld Addr Ptr Hi
Ld Stack Ptr Hi
NOR
Clk
138 output (inv)
Ld Prog Ctr Dummy
Note: The Load Special Pointer logic is Deprecated. It is replaced by the AR Data Bus Load Enable LUT. However, the LUT still needs to NOR its active low output enables with the CLK (exceptions: PC[L] + PC[H] = DHPC Load Enable and SP[L] Load Enable).
Removed

## Slide 18: Address Registers - Data Bus Load Enable v2.0
AR DB LE 8x8 LUT
EEPROM Address Bit | Input
7 | PC Load Branch (ACTIVE LOW)
6 | loadAR (control signal)
5 | PC Load (control signal)
4 | loadARHorL (control signal)
3 | Opcode_MAA (ACTIVE LOW)
2 | (AR) L/H instruction operand
1 | ARDest[1]
0 | ARDest[0]
EEPROM Data Output Bit | Output
7 | BP[H] Load Enable (ACTIVE LOW)
6 | BP[L] Load Enable (ACTIVE LOW)
5 | SP[H] Load Enable (ACTIVE LOW)
4 | SP[L] Load Enable (ACTIVE LOW)
3 | DP[H] Load Enable (ACTIVE LOW)
2 | DP[L] Load Enable (ACTIVE LOW)
1 | DHPC Load Enable (ACTIVE LOW)
0 | PC[L] + PC[H] = DHPC Load Enable (ACTIVE LOW)
µC 8: PC Load
PC Ld Branch
PC Ld En
µC 18: LoadAR H/L
µC 17: LoadAR
Opcode_MAA
Opcode_5
Opcode_7
Opcode_6
DHPC Ld En
DP[L] Ld En
DP[H] Ld En
SP[L] Ld En
SP[H] Ld En
BP[L] Ld En
BP[H] Ld En
Main CLK

## Slide 19: Program Counter (v2.0)
74HC245
74HC161 PC[14:12]
74HC161 PC[11:8]
74HC161 PC[7:4]
74HC161 PC[3:0]
PC Low[7:0]
~Main Reset
Main CLK
INC Prog Counter
74HC245
19
Data
[3:0]
Data
[7:4]
Address Bus
Addr Low
[8:1]
Addr Hi
[15:9, 0]
Program Counter OE
PC[7:0 ] Addr[8:1]
PC[14:8]  Addr[15:9]
INC  Addr[0]
Prog Counter 14:0 are mapped to Address Bus 15:1.
“INC Prog Counter” is mapped to Address Bus bit 0
Relative Branch only update PC 7:0, or Address bus 8:1
Absolute Branch, JSR, RTS use the PC Dummy Reg
PC bit 15 is not used
574: Prog Ctr
Dummy
Data Bus
DHPC Ld En
PC Ld En
PC High
[14:8]
[0]
PC
[7:4]
PC
[3:0]
PC High[14:8]
Note: The PC Loading and output logic is Deprecated.
The PC may not write directly to the Data Bus (remove Read PC Low).
PC Ld Lo and Hi are deprecated, replaced by AR Data Bus Load Enable’s PC[L] + PC[H] = DHPC Load Enable (which goes to both PC[H] and PC[L]).
Ld Prog Ctr Dummy is deprecated, replaced by AR Data Bus Load Enable’s DHPC Load Enable (which must be NOR’d with the CLK signal).

## Slide 20: Load PC High (v2.0)
OpCode_05
OpCode_10
OpCode_11
PC Ld Hi
Branch Absolute
JSR
RTS
Note: The Load PC High logic is Deprecated. It is replaced by AR Data Bus Load Enable’s PC[L] + PC[H] = DHPC Load Enable signal.
Removed

## Slide 21: Data Pointer (v2.0)
!Clk
Control
AND
Clk
21
Address Bus + Read/Write
574: Addr Ptr Lo
A7..A0
A15..A8
574: Addr Ptr Hi
Data Pointer OE
Data
Bus
A7..A0
A15..A8
Note: Ld Addr Ptr Hi is Deprecated. It is replaced by AR Data Bus Load Enable’s DP[H] Load Enable (which needs to be NOR’d with the clock signal).
Note: Data Pointer OE is Deprecated. It is replaced by ARSelect’s DP Output Enable.
Done
Note: Address Pointer Lo’s clock gating is Deprecated. It is replaced by AR Data Bus Load Enable’s DP[L] Load Enable (which needs to be NOR’d with the clock signal). Control Signal 12 may be removed (? – check which instructions need it).
DP[L] Ld En
DP[H] Ld En

## Slide 22: Stack Pointer (v2.0)
169: U/D 4bit
Data
Bus
574: Stack Ptr Page
µC 15: SP Count
µC 16: SP Up/Down
22
Address Bus + Read/Write
A7..A0
A15..A8
A7..A4
245: 3-State
Stack Pointer OE
A3..A0
SP[H] Ld En
SP[L] Ld En
SP 7:4
SP 3:0
Main CLK
169: U/D 4bit

## Slide 23: Fetch State Machine (v2.0)
273 Hi
MR
175
273 Lo
# Reset_microPC
# Main Reset
µC 7: PC Advance
Main CLK
Prog
Data[7:0]
Prog
Data[7:0]
OpCode
[4:0]
H Reg
8 bits
OpCode
[7:5] Flags
OpCode
[7:6] Rd RO
Short H
[15:12]
OpCode
[7:6] Rd RI
OpCode [5] A/I
23
INC Prog Counter
Quiesce
FetchCycle
Extend Quiesce
MSB_Quiesce
# Bus Grant

## Slide 24: Sharing the Data and Address Buses during Fetch Cycle
Data Bus
Address Bus
Last Micro instruction
PC Advance
Addr+1
Inst address A8=1
Program Counter
Low addr
Program Counter
High addr
Ld Low Instruction
Last Instruction
Next Instruction
Control signals
Clock
Next Instruction Low byte
Next Instruction High byte
Ld High Instruction
Ld Instruction
Last clock of an instruction includes the PC_Advance.
In that clock, the Address and Data buses are used by the Program Counter. No other signal using the address or data buses is allowed.
First clock of the next instruction, buses are used to load the high byte of the instruction. To avoid transmission of the first micro instruction on the buses, the micro instruction address bit A8 is set, and all control signals are set to 0, avoiding any transmission on the busses
Micro Instruction 0 controls the buses
Micro
instruction 0
Micro
instruction 1

## Slide 25: PC Advance - Logic Analyzer
PC Advance
Address Bus controlled by Prog Count
Ld Low (rising)
INC, Quiesce
Ld High
(from INC)
Reset Micro Instruction Ctr
CTR=0
CTR=0
CTR=1
CTR=2

## Slide 26: Bus Arbitration for I/O
Normal
CPU owns buses
MMIO Buses Request
No change
CPU owns buses till end of instruction
MMIO Buses Granted
CPU does not transmit on
  Address bus
  Data bus
  Micro instruction controls
Microinstruction counter held in reset
Bus Request
MMIO request
End of
Micro instruction
Bus Release
Extend Quiesce
# Bus Release
Bus Grant
Quiesce
Requested
175
4
5
6
1
2
3
5
4
6
1
2
3
12
13
11

## Slide 27: Micro Instructions EEPROMs (v2.0)
Counter A2..A0
Micro Ins 8_15
1,0,0,0,0,0,0,0
1,0,0,0,0,0,0,0
µC 7: PC Advance
µC 6: Out Reg H
µC 5. Reg In En
µC 4: Reg Out En
µC 3: Reg Out Select
µC 2: ALU Out En
µC 1: ALU Load A
µC 0: ALU Load B
µC 5. Reg In En
µC 4. Reg Out En
Micro Ins 0_7
5 bit
0,0
0,0
3 bit
3 bit
5 bit
Opcode A7..A3
µC 2. ALU Out En
µC 15: SP Count
µC 14: SP Out
µC 13: Reg Out Rd
µC 12: Ld Data Addr
µC 11: MEM Write
µC 10: MEM Read
µC 9: PC Out
µC 8: PC Load
161
3 bit
Main CLK
# Reset_microPC
OpCode
[4:0]
Micro Ins 16_23
1,0,0,0,0,0,0,0
5 bit
0,0
3 bit
µC 23:
µC 22: AB2DB H/L
µC 21: AB2DB
µC 20: TmpARWrite
µC 19: ?
µC 18: LoadAR H/L
µC 17: LoadAR
µC 16: SP Up/Down
27
Set A8 to quiesce all controls during the first clock while upper OpCode is loading
MSB_Quiesce

## Slide 28: SD Card – Page Load / Store
6
7
8
9
10
11
12
13
14
RESET
GND
VCC (3.3v)
VIN (5v)
5V
574 Addr - High
3.3v – 5v
bi-directional
level shifters
8-bit data bus
Addr 15:8
9 - CNT/CLK
10 – RESET Counters
Address | R/W | Register
Base Addr | W | Addr Hi
+1 | W | Sector Hi
+2 | W | Sector Lo
+3 | W | Go
8 - GO_INT
11 - Serial_IN
12 - Shift
17 – ReadRAM#
16 – WriteRAM#
3:0 Ctr
7:4 Ctr
Addr 7:4
Addr 3:0
165 Sector Hi
165 Sector Lo
165 Sector Hi
Data bus
138 Decoder
Load Addr Hi
Ld Sector
Addr 2:0
Data bus
Operation | ReadRAM# | WriteRAM# | Addr_En# | Dat_ dir | SRAM OE# | SRAM WE#
Idle | 0 | 0 | 1 | N/A | N/A | N/A
RAM  SD | 0 | 1 | 0 | In | 0 | 1
SD  RAM | 1 | 0 | 0 | Out | 1 | 0
Idle | 1 | 1 | 1 | N/A | N/A | N/A
Addr_en#
Addr_en#
WriteRAM#
HC245 Data Out
HC245 Addr Out
~SD Card Device En
Addr_en#
28
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Addr_en#
XNOR
#WE
Bus Grant
Bus Request
# Main Reset
# Bus Release

## Slide 29: Counter (v2.0)
Addr 2:0
Read Decoder
Write Decoder
#OE
#WE
~Counter Device En
Addr 2:0
Data Bus
74HC590 Counter
74HC590 Counter
74HC590 Counter
74HC590 Counter
74HC590 Counter
MRC: Reset Counter
CPR: Latch Counter
Address | R/W | Register
Base Addr | W | Reset Counter
+1 | W | Latch Counter
+2 | R | Read Counter 0
+3 | R | Read Counter 1
+4 | R | Read Counter 2
+5 | R | Read Counter 3

## Slide 30: OpCode Decoder (v2.0)
74HC138
OpCodes 24-31
0
1
2
74HC138
OpCodes 8-15
74HC138
OpCodes 0-7
74HC138
OpCodes 16-23
OpCode
[4:0]
0
1
2
3
4
OpCode_6
OpCode_08
OpCode_0D
OpCode_7
‘0’
‘0’
‘1’
30
OpCode_05
OpCode_10
OpCode_11
Branch Absolute
JSR
RTS
Branch Relative
OpCode_1
BRK
ALU Immediate
Out Reg
Out Imm
0
1
2
0
1
2
0
1
2
‘0’
‘0’
OpCode_18
OpCode_19
OpCode_MAG
OpCode_1B
OpCode_1C
OpCode_1D
OpCode_1E
OpCode_1F
MAAL
MAAH
1A
LDA
MGA
Unused
Unused
Unused
OpCode_13
TST Im

## Slide 31
ALU Interface – Flags, A,B Registers, Op Code selection (v2.0)
ALU
ALU OpCode
Flags
Carry In
74HC251
74HC161
Parallel Load Enable
74HC157
4b’0110 (ADD)
Function H[3:0]
OpCode_7
Gray
0
1
Don’t update flags on BR relative
MR
Clock
Clk
Clk
A_I
µC 2. ALU Out En
µC 1: ALU Load A
µC 0: ALU Load B
74HC161
74HC161
Data
Bus
Data Bus
74HC161
74HC161
A
B
C
Flags
Notes: Registers A and B are implemented by two HC161s, each stores 4 bits as the typical HC273 and HC347 won't fit into the 16pin sockets on the ALU wireup board.
The branch relative instruction doesn’t update flag bits to avoid corrupting the flag register state when executing a branch instruction (which may occur due to the ADD operation performed)
Branch Relative

## Slide 32: Output H Register to Data Bus
HC245
H  Bus
HC245
H4  Bus
Data
Bus
If opcode is 00110 (ALU Im) or 10011 (TST Im), only the upper 4 bit of H are used as a lower 4-bit value.
The upper 4-bits are sign extended.
H Reg[7:4]
µC 6: Out Reg H
H Reg
8 bits
32
OpCode_6
OpCode_13
0: H
1: H4
12
13
11
1
2
3
4
5
6
9
10
12

## Slide 33: Branch (v2.0)
74HC151
Flags
74HC161
‘1’
‘N’
‘C’
‘Z’
D4
D5
D6
D7
Q7 Q6 Q5
Instruction LSB
C2 | C1 | C0 | Condition | Instruction LSB | Equivalent Assembly Instruction
0 | 0 | 0 | JMP | 05 | JMP
0 | 0 | 1 | N | 25 | BMI – Branch on Minus
0 | 1 | 0 | C | 45 | BCS – Branch Carry Set
0 | 1 | 1 | Z | 65 | BEQ – Branch Equal
1 | 0 | 0 | Never | 85 | NOP
1 | 0 | 1 | !N | A5 | BPL – Branch on Plus
1 | 1 | 0 | !C | C5 | BCC – Branch Carry Clear
1 | 1 | 1 | !Z | E5 | BNE
µC 8: PC Load
OpCode
[7:5]
PC Ld Branch
Note: PC Ld Lo is renamed to PC Load Branch.

## Slide 34: Instruction set (v2.0)
Op code | Instruction | Details
0x00 | NOP | No operation
0x01 | BRK | Halt the program
0x02 | ALU (Format ALU Rd, Rs1, Rs2) | ALU instruction (OR, AND, XOR, NOT, ADD, SUB, ASL, ROL, LSR, ASR, ROR, ADC, SBC)
0x03 | LDR | Load Register from immediate
0x04 | MOV | Copy Register (MOV instruction in ARM)
0x05 | Branch Absolute | Jump to an address (8bit)
0x06 | ALU Immediate (Format: ALU Rd, Rd, imm) | ALU instruction with value from immediate
0x07 | BRANCH Relative | Relative Branch (+127 to -128)
0x08 | OUT register | Print a register as a character or integer
0x09 | LMA | Load register from address
0x0A | SMA | Store register to address
0x0B | LMR | Load register from address in another register
0x0C | SMR | Store register into an address in another register
0x0D | OUT Immediate | Print the immediate next byte as a character or integer
0x0E | PUSH | 
0x0F | POP | 
0x10 | JSR | Jump Subroutine, store current PC in stack
0x11 | RTS | Return Subroutine, Load PC from stack
0x12 | TST Registers | Compare registers
0x13 | TST Register | Compare register and immediate
0x14 | LDW1 | Load Data Byte with Offset 1 (PC or SP)
0x15 | LDW2 | Load Data Byte with Offset 2 (DP or BP)
0x16 | SDW1 | Store Data Byte with Offset 1 (PC or SP)
0x17 | SDW2 | Store Data Byte with Offset 2 (DP or BP)
0x18 | MAA1 | Move Address with Offset to Address 1 (PC or SP)
0x19 | MAA2 | Move Address with Offset to Address 2 (DP or BP)
0x1A | MAG | Move Address to General register
0x1B | LDA | Load Address register
0x1C | MGA | Move General to Address register
Covered by BIST
Completed
Planned
Deprecating
34

## Slide 35: ALU with changes
Op Select | Special Func. = 0 |  | Special Func. = 1 |  | Flag in | Flags Out
0 | A OR B | OR: 0 | A OR B |  | - | Z, N
1 | A AND B | AND: 2 | A AND B |  | - | 
2 | A XOR B | XOR: 4 | ~B | NOT: 5 | - | Z, N
3 | A + B | ADD: 6 | A – B | SUB: 7 | - | Z, N, Co
4 | Shift Left A A[0]=0 | ASL: 8 | Rotate left A A[0]=Cin | ROL: 9 | Cin (Rotate) | Z, N=A[6], Co=A[7]
5 | Shift Right A | LSR: A | Arithmetic S.R. A | ASR: B | - | Z, N, Co=A[0]
6 | Rotate Right | ROR: C | Cin -> A-> Cout |  | Cin | Z, N, Co=A[0]
7 | A + B + Cin | ADC: E | A – B + Cin | SBC: F | Cin | Z, N, Co
Proposals for the additional operations
How to chain Shift Right of two bytes?
Proposal | # of IC slots | Description | Op Code
OR and ADD share Op Code (low priority) | 2x 74LS157 | Special Function select OR or AND | Release op code
Allow using ALU as two registers (low Priority) |  | Need to create output A and B | 
35

## Slide 36: Micro-Instructions Control: NOP Instruction (00000)
Cycle # | Instruction | Explanation
0 | 00000000 = 0x00 | 
1 | 10000000 = 0x80 | Increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
0
NOP
36
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
None | XX | X | XXXX | XX | X | OpCode=00

## Slide 37: Micro-Instructions Control: BREAK (00001)
Cycle # | Instruction | Explanation
0 | 00000000 = 0x00 | Do nothing
1 | 10000000 = 0x80 | Increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
1
BRK
37
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Note: BRK has the same microcode as NOP, but the opcode decoder halts the clock when the opcode 00001 is detected. Stepping through it manually (via Single-Step / Run button press) resumes the clock. Hence, BRK acts as a hardware breakpoint.
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
None | XX | X | XXXX | XX | X | OpCode=01

## Slide 38: Micro-Instructions Control: ALU (00010)
Cycle # | Instruction | Explanation
0 | 00010010 = 0x12 | Load Rs1 to reg A
1 | 00011001 = 0x19 | Load Rs2 to reg B
2 | 00100100 = 0x24 | Output and Read to Rd
3 | 10000000 = 0x80 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
ALU | Rs2 | Rs1 | S2 S1 S0 SF (Function sel) | Rd | X | OpCode=02
2
ADD Rd, Rs1, Rs2
38
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 39: Micro-Instructions Control: Load Immediate to Reg (00011)
Cycle # | Instruction | Explanation
0 | 01100000 = 0x60 | Write imm to bus and Rd read
1 | 10000000 = 0x80 | Increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Imm | Immediate (8-bit) |  | Immediate (8-bit) | Rd | X | OpCode=03
3
LDR Rd, #0x00
39
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 40: Micro-Instructions Control: MOV (00100)
Cycle # | Instruction | Explanation
0 | 00110000 = 0x30 | Write Rs1 to bus and Rd reads
1 | 10000000 = 0x80 | Increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | XX | Rs1 | XXXX | Rd | X | OpCode=04
4
MOV Rd, Rs1
40
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 41: Micro-Instructions Control: Branch / Jump Absolute Immediate (00101)
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 5 | 4 3 2 1 0
Branch | Immediate (8-bit) |  | Immediate (8-bit) | C2 C1 C0 | OpCode=05
Cycle # | Instruction | Explanation
0 | 0x1_40 01_0100_0000 | Write H register to bus and PC (conditionally) reads
1 | 0x0_80 00_1000_0000 | PC advance
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
C2 | C1 | C0 | Condition | Low instruction register | Assembly
0 | 0 | 0 | JMP | 05 | JMP
0 | 0 | 1 | N | 25 | BMI – Branch on Minus
0 | 1 | 0 | C | 45 | BCS – Branch Carry Set
0 | 1 | 1 | Z | 65 | BEQ – Branch Equal
1 | 0 | 0 | Never | 85 | NOP
1 | 0 | 1 | !N | A5 | BPL – Branch on Plus
1 | 1 | 0 | !C | C5 | BCC – Branch Carry Clear
1 | 1 | 1 | !Z | E5 | BNE
5
41
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 42: Micro-Instructions Control: ALU immediate (4-bit) (00110)
Cycle # | Instruction | Explanation
0 | 10_0000_0001_0010 = 2012 | Load Rd to reg A
1 | 0100_0001 = 0x0041 | Load 4 bit imm to reg B
2 | 0010_0100 = 0x0024 | Write ALU output to Rd
3 | 1000_0000 = 0x0080 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
Type | 15 14 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
ALU | 4-bit imm. | S2 S1 S0 SF (Function sel) | Rd | X | OpCode=06
6
ADD Rd, #0x00
42
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 43: Micro-Instructions Control: Branch / Jump Relative Immediate (00111)
Cycle # | Instruction | Explanation
0 | 10_0000_0010 0x2_02 | Load PC into reg A
1 | 00_0100_0001 0x0_41 | Load immediate into reg B
2 | 01_0000_0100 0x1_04 | Output ALU val, load PC
3 | 00_1000_0000 0x0_80 | Advance PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
C2 | C1 | C0 | Condition | OpCode | Assembly
0 | 0 | 0 | JMP | 07 | JMP
0 | 0 | 1 | N | 27 | BMI – Branch on Minus
0 | 1 | 0 | C | 47 | BCS – Branch Carry Set
0 | 1 | 1 | Z | 67 | BEQ – Branch Equal
1 | 0 | 0 | Never | 87 | NOP
1 | 0 | 1 | !N | A7 | BPL – Branch on Plus
1 | 1 | 0 | !C | C7 | BCC – Branch Carry Clear
1 | 1 | 1 | !Z | E7 | BNE
7
43
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 5 | 4 3 2 1 0
Branch | Immediate (8-bit) |  | Immediate (8-bit) | C2 C1 C0 | OpCode=07
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Note: This only sets the PC Low register! As such, this instruction is Deprecated.

## Slide 44: Micro-Instructions Control: OUT (01000) (Display ASCII or Integer)
Cycle # | Instruction | Explanation
0 | 0000_0000 = 0x00 | Wait for H register to be loaded (need value of Rs1)- No longer required
1 | 0001_0000 = 0x10 | Write Rs1 to the bus (when opcode 01000 is detected, the value on the bus is read by the OUT register to the display)
2 | 1000_0000 = 0x80 | Advance PC
3 |  | 
4 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Reg | OpCode | XX | Rd | XXXX | Rs1 | XX
8
OUT Rs1, A
44
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Out | XX | Rs1 | XXXX | XX | I=1; A=0 | OpCode=08
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 45: Micro-Instructions Control: LMA (Load Memory Absolute) (01001)
Cycle # | Instruction | Explanation
0 | 1_0000_0100_0000 = 1040 | Load 8-bit address to address register
1 | 0_0100_0010_0000 = 0420 | Read byte from RAM and store in Rd
2 | 0_0000_1000_0000 = 0080 | Increment PC
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
9
Type | 15 14 13 12 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | 8-bit (LSBs) Address | Rd | X | OpCode=09
LMA Rd, #Addr
45
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Removed

## Slide 46: Micro-Instructions Control: SMA (Store Memory Absolute) (01010)
Cycle # | Instruction | Explanation
0 | 01_0000_0100_0000 = 1040 | Load 8-bit address to address register
1 | 10_1000_0001_0000 = 2810 | Store byte to RAM from Rd
2 | 00_0000_1000_0000 = 0080 | Increment PC
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
A
Type | 15 14 13 12 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | 8-bit (LSBs) Address | Rd | X | OpCode=0A
SMA Rd, #Addr
46
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Removed

## Slide 47: Micro-Instructions Control: LMR (Load Memory Register) (01011)
Cycle # | Instruction | Explanation
0 | 1_0000_0001_0000 = 1010 | Load Rs1 to Address Register
1 | 0_0100_0010_0000 = 0420 | Load value at the address into Rd
2 | 0_0000_1000_0000 = 0080 | Increment PC
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | XX | Rs1 | XXXX | Rd | X | OpCode=0B
LMR Rd, Rs
47
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Effect: Rd = *Rs
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Removed

## Slide 48: Micro-Instructions Control: SMR (Store Memory Register) (01100)
Cycle # | Instruction | Explanation
0 | 01_0000_0001_0000 = 1010 | Load Rs1 to Address Register
1 | 10_1000_0001_0000 = 2810 | Store value at Rd to RAM
2 | 00_0000_1000_0000 = 0080 | Increment PC
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
C
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | XX | Rs1 | XXXX | Rd | X | OpCode=0C
SMR Rd_data, Rs1_addr
48
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Removed

## Slide 49: Micro-Instructions Control: OUT immediate (01101)
Cycle # | Instruction | Explanation
0 | 0000_0000 = 0x00 | Wait for H instruction register to be loaded
1 | 0100_0000 = 0x40 | Write program register H to the bus
2 | 1000_0000 = 0x80 | Advance PC
3 |  | 
4 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Reg | OpCode | XX | Rd | XXXX | Rs1 | XX
D
OUT #Imm, A
49
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Out | 8-bit immediate |  | XXXX | XX | I=1; A=0 | OpCode=0D
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 50: Micro-Instructions Control: PUSH (01110)
Cycle # | Instruction | Explanation
0 | 0_0100_1000_0001_0000 = 0x04810 | Store Rs1 in the stack
1 | 1_1000_0000_1000_0000 = 0x18080 | Increment stack pointer (and increment PC)
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
E
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | XX | Rs1 | XXXX | XX | X | OpCode=0E
PUSH Rs1
50
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Removed

## Slide 51: Micro-Instructions Control: POP (1111)
Cycle # | Instruction | Explanation
0 | 0_0000_0000_0000_0000 = 0x00000 | Wait for next clock
1 | 0_1000_0000_0000_0000 = 0x08000 | Decrement stack pointer
2 | 0_0100_0100_0010_0000 = 0x04420 | Load value from stack to Rd
3 | 0_0000_0000_1000_0000 = 0x00080 | Increment PC
4 |  | 
5 |  | 
6 |  | 
F
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | XX | XX | XXXX | Rd | X | OpCode=0F
POP Rd
51
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Removed

## Slide 52: Micro-Instructions Control: JSR Jump Subroutine (10000)
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 0_0100_1010_0000_0000 = 0x04A00 | Write PC to stack
1 | 1_1000_0000_0000_0000 = 0x18000 | Increase stack pointer
2 | 0_0000_0001_0100_0000 = 0x00140 | Jump to immediate address
3 | 0_0000_0000_1000_0000 = 0x00080 | Advance PC
4 |  | 
5 |  | 
6 |  | 
10
Type | 15 14 13 12 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | 8-bit Immediate (Program Address) | XX | X | OpCode=10
JSR #Imm
52
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Removed

## Slide 53: Micro-Instructions Control: RTS Return from Subroutine (10001)
Cycle # | Instruction | Explanation
0 | 00_1000_0000_0000_0000 = 0x08000 | Decrement stack pointer
1 | 00_1000_0000_0000_0000 = 0x08000 | Decrement stack pointer
2 | 10_0100_0100_0000_0000 = 0x24400 | Load Dummy from stack
3 | 01_1000_0000_0000_0000 = 0x18000 | Increment SP
4 | 00_0100_0101_0000_0000 = 0x04500 | Load program address on the stack to the program counter
5 | 00_1000_0000_1000_0000 = 0x08080 | Decrement SP, Advance PC
11
Type | 15 14 13 12 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | XXXX XXXX | 00 | X | OpCode=11
RTS
53
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Stack Pos | Expected Data
Start SP | Empty
Start SP - 1 | Return Address Low Byte
Start SP – 2 | Return Address High Byte
Note: Return address must be 16-bit! I.e., to jump to a subroutine, you must use:
PUSH Return Address High Byte
LSP DummyPC, Subroutine Address High Byte
JSR Subroutine Address Low Byte
Note: Bits 7-6 MUST be 00 so that the special pointer is specified as DHPC
(for cycle 2).

## Slide 54: Micro-Instructions Control: Test (10010)
Cycle # | Instruction | Explanation
0 | 0001_0010 = 0x12 | Load Rs1 to reg A
1 | 0001_1001 = 0x19 | Load Rs2 to reg B
2 | 0000_0100 = 0x04 | Output ALU value on bus (but don’t save in register)
3 | 1000_0000 = 0x80 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
ALU | Rs2 | Rs1 | S2 S1 S0 SF (Function sel) | XX | X | OpCode=12
TST Rs1, Rs2
12
54
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 55: Micro-Instructions Control: Test immediate (10011)
Cycle # | Instruction | Explanation
0 | 10_0000_0001_0010 = 0x2012 | Load Rd to reg A
1 | 0100_0001 = 0x0041 | Load 4 bit imm to reg B
2 | 0000_0100 = 0x0004 | Write ALU output to bus (but not to register)
3 | 1000_0000 = 0x80 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
Type | 15 14 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
ALU | 4-bit imm. | S2 S1 S0 SF (Function sel) | Rd | X | OpCode=13
TST Rd, #0x00
13
55
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 56: Micro-Instructions Control: Load Special Register (Immediate) (10100)
Cycle # | Instruction | Explanation
0 | 10_0000_0000_0100_0000 = 0x20040 | Loads 8-bit immediate to specified special register
1 | 00_0000_0000_1000_0000 = 0x00080 | Increment PC
2 |  | 
3 |  | 
56
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Branch | Immediate (8-bit) |  | Immediate (8-bit) | C1 C0 | X | OpCode=14
14
C1 | C0 | Special Register | Command Parameter
0 | 0 | PC (High Byte) | PC
0 | 1 | Data Pointer (High Byte) | DP
1 | 0 | Stack Pointer (High Byte) | SP
1 | 1 | N/A (in future, perhaps a Frame Pointer (High Byte)) | 
LSP DP, #0x00

## Slide 57: New Addressing Modes
New architectural perspective:
Two kinds of words exist (data words (8 bit) and address words (16 bit)).
Each kind of words have their own registers (data registers and address registers), register files, and dedicated busses (data bus and address bus).
Programming Model-wise, moving towards using Address Registers for all pointer use; i.e., to perform memory loads/stores, an address register must be set to the relevant address and then used. The additional instruction overhead of this (setting the address register using an immediate / GR which takes at least 2 instructions for high and low bytes) is reduced by allowing for 8 bit immediate offsets and by setting an AR to another AR (with offset) in a single instruction.
Instruction Type | New Instruction Semantics | Instruction Operands | Opcodes Used
AR  GR | Rd = ARSrc[L/H] | Rd (2 bits), ARSrc (2 bits), L/H (1 bit) | 1
Memory  GR | Rd = *(ARSrc + Imm) | Rd (2 bits), ARSrc (2 bits), Imm (8 bits) | 2 (need two opcodes to account for ARSrc being 2 bits, but only having 1 bit for the operand in instruction string)
Immediate  AR | ARDest[L/H] = Imm | ARDest (2 bits), L/H (1 bit), Imm (8 bits) | 1
GR  AR | ARDest[L/H] = Rs1 | ARDest (2 bits), L/H (1 bit), Rs1 (2 bits) | 1
AR  AR | ARDest = ARSrc + Imm | ARDest (2 bits), ARSrc (2 bits), Imm (8 bits) | 2 (need two opcodes to account for ARSrc being 2 bits, but only having 1 bit for the operand in instruction string)
GR  Memory | *(ARSrc + Imm) = Rs | ARSrc (2 bits), Imm (8 bits), Rs (2 bits) | 2 (need two opcodes to account for ARSrc being 2 bits, but only having 1 bit for the operand in instruction string)
Total opcodes needed: 9
But, can offset this by removing:
LSP (1)
PUSH / POP (2)
Current load-store memory instructions (4)
OUT instructions (2) (need to make display interface part of MMIO)

## Slide 58: ByteFrost Instruction Decode
Instruction Operand | Number of Bits | Location
Opcode | 5 | 4:0
Rs1 | 2 | 13:12
Rs2 | 2 | 15:14
Rd | 2 | 7:6
ALU Function | 4 | 11:8
Immediate (8) | 8 | 15:8
Immediate (4) | 4 | 15:12
Branch Condition | 3 | 7:5
A/I (Display) | 1 | 5
AR L/H | 1 | 5
ARSrc | 1 or 2 | Special Case – See Sidebar
ARDest | 2 | 7:6
Decode Module
Instruction String (16 bits)
Instruction operands (Opcode, Rd, Rs1, …)
ARSrc Decode:
If opcode is of (AR  GR) (Rd = ARSrc[L/H]) instruction, then ARSrc is in bits 9:8.
Otherwise, ARSrc is a function of bits 5 and the opcode (maybe the opcode’ least significant bit?)
Instructions that specify ARSrc with 1 bit in bit 5 need to get the other bit from the opcode; if we always assign these two-opcode instructions opcodes as [4-bit opcode x][0/1], then we can get the other ARSrc bit from the least significant bit of the opcode, i.e., in these instructions ARSrc is {Instr[5], Instr[0]} (in bits 5 and 0)
Note: Decode module always creates values for all operands, even those that don’t exist in the current instruction (e.g., no Immediate in the opcode 2 ALU instruction). It’s up to the microcode to specify which operands to read / use to avoid reading garbage data.

## Slide 59: New Addressing Mode Instructions
Type | 15 14 13 12 11 10 | 9 8 | 7 6 | 5 | 4 3 2 1 0
 | XXXXXX | ARSrc | Rd | L/H | OpCode
(AR  GR) Rd = ARSrc[L/H]
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
 | Immediate (8-bit) |  | Immediate (8-bit) | Rd | ARSrc | OpCode (bit 0 is part of ARSrc)
(Memory  GR) Rd = *(ARSrc + Imm)
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
 | Immediate (8-bit) |  | Immediate (8-bit) | Rd | ARSrc | OpCode (bit 0 is part of ARSrc)
(GR  Memory) *(ARSrc + Imm) = Rs (Rd as source)
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
 | Immediate (8-bit) |  | Immediate (8-bit) | ARDest | L/H | OpCode
(Imm  AR) ARDest[L/H] = Imm
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
 | XX | Rs1 | XXXX | ARDest | L/H | OpCode
(GR  AR) ARDest[L/H] = Rs1
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
 | Immediate (8-bit) |  | Immediate (8-bit) | ARDest | ARSrc | OpCode (bit 0 is part of ARSrc)
(AR  AR) ARDest = ARSrc + Imm

## Slide 60: (AR  GR) Instruction
Type | AR  GR
Semantics | Rd = ARSrc[L/H]
Number of Opcodes Required | 1
Operands | Rd (2 bits), ARSrc (2 bits), L/H (1 bit)
Additional Inputs | ARSelect, AddressByteSelect
Control Signals Needed | AddressBusToDataBus
Cycle # | Instruction | Explanation
0 | ARSelect = ARSrc | Write ARSrc to the Address Bus.
 | AddressByteSelect = L/H (default behavior) | Write Address Bus L/H byte to the Data Bus.
 | AddressBusToDataBus = 1 | 
 | RegisterFileInputEnable = 1 | Set Rd to read from the Data Bus.
Non-control signals are marked as bold. Control signals are marked as italic.

## Slide 61: (Memory  GR) Instruction
Type | Memory  GR
Semantics | Rd = *(ARSrc + Imm)
Number of Opcodes Required | 2
Operands | Rd (2 bits), ARSrc (2 bits), Imm (8 bits)
Additional Inputs | ARSelect
Control Signals Needed | TmpARRead
Cycle # | Instruction | Explanation
0 | Program Register H Write to Bus = 1 | Write Imm to the Data Bus.
 | ARSelect = ARSrc | Write ARSrc to the Address Bus.
 | TmpARRead = 1 | Set TmpAR to read (from the 16-bit adder).
1 | ARSelect = TmpAR | Write TmpAR to the Address Bus.
 | MemRead = 1 | Write Memory data word to the Data Bus.
 | RegisterFileInputEnable = 1 | Set Rd to read from the Data Bus.
Non-control signals are marked as bold. Control signals are marked as italic.

## Slide 62: (Imm  AR) Instruction
Type | Immediate  AR
Semantics | ARDest[L/H] = Imm
Number of Opcodes Required | 1
Operands | ARDest (2 bits), L/H (1 bit), Imm (8 bits)
Additional Inputs | 
Control Signals Needed | LoadAR (currently Load Special Register)
Cycle # | Instruction | Explanation
0 | Program Register H Write to Bus = 1 | Write Imm to the Data Bus.
 | LoadAR = 1 | Set ARDest[L/H] to read from the Data Bus.
Non-control signals are marked as bold. Control signals are marked as italic.

## Slide 63: (GR  AR) Instruction
Type | GR  AR
Semantics | ARDest[L/H] = Rs1
Number of Opcodes Required | 1
Operands | ARDest (2 bits), L/H (1 bit), Rs1 (2 bits)
Additional Inputs | 
Control Signals Needed | LoadAR (currently Load Special Register)
Cycle # | Instruction | Explanation
0 | Register File Output Enable = 1 | Write Rs1 to the Data Bus.
 | RegisterFileOutputSelect = 0 (Rs1) | 
 | LoadAR = 1 | Set ARDest[L/H] to read from the Data Bus.
Non-control signals are marked as bold. Control signals are marked as italic.

## Slide 64: (AR  AR) Instruction
Type | AR  AR
Semantics | ARDest = ARSrc + Imm
Number of Opcodes Required | 2
Operands | ARDest (2 bits), ARSrc (2 bits), Imm (8 bits)
Additional Inputs | ARSelect, AddressByteSelect
Control Signals Needed | AddressBusToDataBus, loadAR, loadARHorL
Cycle # | Instruction | Explanation
0 | Program Register H Write to Bus = 1 | Write Imm to the Data Bus.
 | ARSelect = ARSrc | Write ARSrc to the Address Bus.
 | TmpARRead = 1 | Set TmpAR to read.
1 | ARSelect = TmpAR | Write TmpAR to the Address Bus.
 | AddressBusToDataBus = 1 | Write low byte of the Address Bus to the Data Bus.
 | AddressByteSelect = 0 (L) | 
 | loadAR = 1 | Set ARDest[L] to read from the Data Bus.
 | loadARHorL = 0 (L) | 
2 | ARSelect = TmpAR | Write TmpAR to the Address Bus.
 | AddressByteSelect = 1 (H) | Write high byte of the Address Bus.
 | loadAR = 1 | Set ARDest[H] to read from the Data Bus.
 | loadARHorL = 1 (H) | 
Non-control signals are marked as bold. Control signals are marked as italic.

## Slide 65: (GR  Memory) Instruction
Type | GR  Memory
Semantics | *(ARSrc + Imm) = Rs (Rd as source)
Number of Opcodes Required | 2
Operands | ARSrc (2 bits), Imm (8 bits), Rd (2 bits)
Additional Inputs | ARSelect
Control Signals Needed | TmpARRead, TmpARWrite
Cycle # | Instruction | Explanation
0 | Program Register H Write to Bus = 1 | Write Imm to the Data Bus.
 | ARSelect = ARSrc | Write ARSrc to the Address Bus.
 | TmpARRead = 1 | Set TmpAR to read.
1 | ARSelect = TmpAR | Write TmpAR to the Address Bus.
 | Register File Output Enable = 1 | Write Rs (Rd) to the Data Bus.
 | Use Rd as Source = 1 | 
 | MemWrite = 1 | Set Memory to read from the Data Bus.
Non-control signals are marked as bold. Control signals are marked as italic.

## Slide 66: ARSelect
Bus Grant | FetchCycle | PC Out control signal | SP Out control signal | TmpAR Write control signal | Opcode_MAG_LDW_SDW_MAA (Active Low) | AR Src operand | Output
1 | X | X | X | X | X | X | None
0 | 1 | X | X | X | X | X | PC
0 | 0 | 1 | X | X | X | X | PC
0 | 0 | 0 | 1 | X | X | X | SP
0 | 0 | 0 | 0 | 1 | X | X | TmpAR
0 | 0 | 0 | 0 | 0 | MAG, LDW, SDW, MAA | AR Src | AR Src (PC, DP, SP, or BP)
0 | 0 | 0 | 0 | 0 | Other Opcodes | X | DP
ARSelect specifies which AR gets to write to the Address Bus and whether any of them do (it can do this since it only sends output enables; if it doesn’t send an output enable to any hardware entity, then no entity writes to the address bus).
Inputs: SP Addr control signal, FetchCycle (output of fetch state machine), Bus Grant (cause bus to float to allow external entity to write on the Address Bus), other control signals, instruction string operands.
Outputs: {None (Address Bus floats), PC, DP, SP, BP, TmpAR} (3 bits)

## Slide 67: ARSelect LUT
The ARSelect combinational logic (explained in previous slide) is implemented as a (8 bit  5 bit) (256 byte) LUT in an EEPROM.
EEPROM Address Bit | Input
7 | Bus Grant
6 | FetchCycle
5 | PC Out (control signal)
4 | SP Out (control signal)
3 | TmpARWrite (control signal)
2 | OPCODE_MAG_LDW_SDW_MAA (ACTIVE LOW)
1 | ARSrc[1] instruction operand
0 | ARSrc[0] instruction operand
EEPROM Data Output Bit | Output
7 | 1 (unused)
6 | 1 (unused)
5 | 1 (unused)
4 | TmpAR Output Enable (ACTIVE LOW)
3 | BP Output Enable (ACTIVE LOW)
2 | SP Output Enable (ACTIVE LOW)
1 | DP Output Enable (ACTIVE LOW)
0 | PC Output Enable (ACTIVE LOW)

## Slide 68: AddressByteSelect
AddressByteSelect selects whether the high (H) or low (L) byte of the Address Bus should be written to the Data Bus (which will be written to the Data Bus if the AddressBusToDataBus control signal is high).
Inputs: L/H instruction operand (1 bit), AddressHorL control signal, Opcode
Output: {Low, High} (1 bit)
Opcode | AddressHorL control signal | L/H instruction operand | Output
MAA or JSR | HorL | X | HorL
Other Opcodes | X | L/H | L/H

## Slide 69: (Data Bus  AR) Loading
We must be able to tell an AR to read from the Data Bus, and we must specify which byte (L or H) it should write the Data Bus’ data word into.
Inputs: L/H instruction operand (1 bit), ARDest instruction operand (2 bits), loadAR control signal, PC Load control signal, loadARHorL control signal, opcode
Output: {None (no AR reads), PC[Dummy H], PC[L], SP[H], SP[L], DP[H], DP[L], BP[H], BP[L]}
(Note: Can’t write to the actual PC H, can only write to the PC Dummy H from the data bus! Actual PC H only reads from the Dummy PC High!)
PC Load Branch (active low) | loadAR control signal | PC Load control signal | Opcode_MAA (active low) | loadARHorL control signal | L/H instruction operand | Output
Active (0) | X | X | X | X | X | PC[L] (and PC[H] = DHPC)
Inactive (1) | 1 | 1 | X | HorL | X | PC[HorL] (if L, PC[L] = data bus and PC[H] = DHPC)
Inactive (1) | 1 | 0 | MAA | HorL | X | ARDest[HorL]
Inactive (1) | 1 | 0 | Other Opcodes | X | L/H | ARDest[L/H]
Inactive (1) | 0 | X | X | X | X | None

## Slide 70: (Data Bus  AR) Loading (AR Data Bus Load Enable LUT)
The Data Bus  AR Loading combinational logic (explained in previous slide) is implemented as a (8 bit  8 bit) (256 byte) LUT in an EEPROM.
EEPROM Address Bit | Input
7 | PC Load Branch (ACTIVE LOW)
6 | loadAR (control signal)
5 | PC Load (control signal)
4 | loadARHorL (control signal)
3 | Opcode_MAA (ACTIVE LOW)
2 | (AR) L/H instruction operand
1 | ARDest[1]
0 | ARDest[0]
EEPROM Data Output Bit | Output
7 | BP[H] Load Enable (ACTIVE LOW)
6 | BP[L] Load Enable (ACTIVE LOW)
5 | SP[H] Load Enable (ACTIVE LOW)
4 | SP[L] Load Enable (ACTIVE LOW)
3 | DP[H] Load Enable (ACTIVE LOW)
2 | DP[L] Load Enable (ACTIVE LOW)
1 | DHPC Load Enable (ACTIVE LOW)
0 | PC[L] + PC[H] = DHPC Load Enable (ACTIVE LOW)

## Slide 71: Micro-Instructions Control: PUSH (01110)
Cycle # | Instruction | Explanation
0 | 0x00_80_00 | (SP--;) Decrement SP.
1 | 0x00_48_10 | (*SP = Rs1;) Write Rs1 to the Data Bus, Write SP to the Address Bus, and Set Memory to read from the Data Bus.
2 | 0x00_00_80 | Advance PC.
71
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
PUSH | XX | Rs1 | XXXX | XX | X | OpCode=0x0e
E
PUSH R2
SP--; *SP = Rs1

## Slide 72: Micro-Instructions Control: POP (01111)
Cycle # | Instruction | Explanation
0 | 0x01_c4_20 | (Rd = *SP; SP++;) Write SP to the Address Bus, Set Memory to write to the Data Bus, Set Rd to read from the Data Bus, and increment SP.
1 | 0x00_00_80 | Advance PC.
72
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
POP | XX | XX | XXXX | Rd | X | OpCode=0x0f
F
POP R1
Rd = *SP; SP++

## Slide 73: Micro-Instructions Control: JSR (10000)
Cycle # | Instruction | Explanation
0 | 0x00_82_00 | (SP--; Address Bus Register High = PC[H];) Decrement SP and Write PC to the Address Bus.
1 | 0x60_c8_00 | (*SP = PC[H]; SP--;) Write SP to the Address Bus, Write Address Bus Register High to the Data Bus (PC[H]), Set Memory to read from the Data Bus, and decrement SP.
2 | 0x00_02_00 | (Address Bus Register Low = PC[L]) Write PC to the Address Bus.
3 | 0x20_48_00 | (*SP = PC[L]) Write SP to the Address Bus, write Address Bus Register Low to the Data Bus (PC[L]), and set Memory to read from the Data Bus.
4 | 0x00_00_00 | (Address Bus Register High = DP[H]) Write DP to the Address Bus.
5 | 0x66_01_00 | (DHPC = DP[H]; Address Bus Register Low = DP[L]) Write DP to the Address Bus, write Address Bus Register High to the Data Bus (DP[H], and set DHPC to load from the Data Bus.
6 | 0x22_01_00 | (PC[L] = DP[L] (and PC[H] = DHPC)) Write Address Bus Register Low to the Data Bus (DP[L]) and set PC[L] to load from the Data Bus.
7 | 0x00_00_80 | Advance PC.
73
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
JSR | XX | XX | XXXX | XX | X | OpCode=0x10
10
JSR
SP--; *SP = PC[H]; SP--;
*SP = PC[L]; PC = DP;

## Slide 74: Micro-Instructions Control: RTS (10001)
Cycle # | Instruction | Explanation
0 | 0x01_80_00 | (SP++;) Increment SP.
1 | 0x06_c5_00 | (DHPC = *SP; SP--;) Write SP to the Address Bus, Set Memory to write to the Data Bus, Set DHPC to read from the Data Bus, and decrement SP.
2 | 0x03_c5_00 | (PC[L] = *SP; SP++;) Write SP to the Address Bus, Set Memory to write to the Data Bus, Set PC[L] to read from the Data Bus (and PC[H] = DHPC), and increment SP.
3 | 0x01_80_80 | (SP++;) Increment SP and Advance PC.
74
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
POP | XX | XX | XXXX | Rd | X | OpCode=0x0f
11
RTS
SP++; DHPC = *SP; SP--;
PC[L] = *SP, PC[H] = DHPC;
SP++; SP++;

## Slide 75: Micro-Instructions Control: Load Data Byte with Offset 1 (LDW1) (10100)
Cycle # | Instruction | Explanation
0 | 0x08_00_40 | Write Imm to the Data Bus, ARSrc to the Address Bus, and set TmpAR to read from the 16-bit adder.
1 | 0x10_04_20 | Write TmpAR to the Address Bus, Write Memory data word to the Data Bus, and set Rd to read from the Data Bus.
2 | 0x00_00_80 | Advance PC.
75
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
LDW | Immediate (8-bit) |  | Immediate (8-bit) | Rd | ARSrc[1] | OpCode=14 (and ARSrc[0] = 0)
14
INSTR[5] | INSTR[0] | ARSrc Address Register | Command Parameter
0 | 0 | PC ({PC[H], PC[L]}) | %PC
1 | 0 | SP | %SP
LDW R2, 16(%SP)
Rd = *(ARSrc + Imm)

## Slide 76: Micro-Instructions Control: Load Data Byte with Offset 2 (LDW2) (10101)
Cycle # | Instruction | Explanation
0 | 0x08_00_40 | Write Imm to the Data Bus, ARSrc to the Address Bus, and set TmpAR to read from the 16-bit adder.
1 | 0x10_04_20 | Write TmpAR to the Address Bus, Write Memory data word to the Data Bus, and set Rd to read from the Data Bus.
2 | 0x00_00_80 | Advance PC.
76
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
LDW | Immediate (8-bit) |  | Immediate (8-bit) | Rd | ARSrc[1] | OpCode=15 (and ARSrc[0] = 1)
15
INSTR[5] | INSTR[0] | ARSrc Address Register | Command Parameter
0 | 1 | DP | %DP
1 | 1 | BP | %BP
LDW R2, 16(%BP)
Rd = *(ARSrc + Imm)

## Slide 77: Micro-Instructions Control: Store Data Byte with Offset 1 (SDW1) (10110)
Cycle # | Instruction | Explanation
0 | 0x08_00_40 | Write Imm to the Data Bus, write ARSrc to the Address Bus, and set TmpAR to read.
1 | 0x10_28_10 | Write TmpAR to the Address Bus, write Rs (Rd) to the Data Bus, and set Memory to read from the Data Bus.
2 | 0x00_00_80 | Advance PC.
77
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
SDW | Immediate (8-bit) |  | Immediate (8-bit) | Rs (Rd) | ARSrc[1] | OpCode=16 (and ARSrc[0] = 0)
16
INSTR[5] | INSTR[0] | ARSrc Address Register | Command Parameter
0 | 0 | PC ({PC[H], PC[L]}) | %PC
1 | 0 | SP | %SP
SDW R2, 16(%SP)
*(ARSrc + Imm) = Rs (Rd as source)

## Slide 78: Micro-Instructions Control: Store Data Byte with Offset 2 (SDW2) (10111)
Cycle # | Instruction | Explanation
0 | 0x08_00_40 | Write Imm to the Data Bus, write ARSrc to the Address Bus, and set TmpAR to read.
1 | 0x10_28_10 | Write TmpAR to the Address Bus, write Rs (Rd) to the Data Bus, and set Memory to read from the Data Bus.
2 | 0x00_00_80 | Advance PC.
78
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
SDW | Immediate (8-bit) |  | Immediate (8-bit) | Rs (Rd) | ARSrc[1] | OpCode=17 (and ARSrc[0] = 1)
17
INSTR[5] | INSTR[0] | ARSrc Address Register | Command Parameter
0 | 1 | DP | %DP
1 | 1 | BP | %BP
SDW R2, 16(%BP)
*(ARSrc + Imm) = Rs (Rd as source)

## Slide 79: Micro-Instructions Control: Address with Offset to Address 1 (MAA1) (11000)
Cycle # | Instruction | Explanation
0 | 0x08_00_40 | Write Imm to the Data Bus, ARSrc to the Address Bus, and set TmpAR to read.
1 | 0x10_00_00 | Write TmpAR to the Address Bus.
2 | 0x32_00_00 | Write TmpAR to the Address Bus, Address Bus Low register to the Data Bus, and set ARDest[L] to read from the Data Bus.
3 | 0x66_00_00 | Write Address Bus High Register to the Data Bus and set ARDest[H] to read from the Data Bus.
4 | 0x_00_00_80 | Advance PC.
79
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
MAA | Immediate (8-bit) |  | Immediate (8-bit) | ARDest | ARSrc[1] | OpCode=18 (and ARSrc[0] = 0)
18
MAA %SP, %SP, #-1
ARDest = ARSrc + Imm
INSTR[5] | INSTR[0] | ARSrc Address Register | Command Parameter
0 | 0 | PC ({PC[H], PC[L]}) | %PC
1 | 0 | SP | %SP

## Slide 80: Micro-Instructions Control: Address with Offset to Address 2 (MAA2) (11001)
Cycle # | Instruction | Explanation
0 | 0x08_00_40 | Write Imm to the Data Bus, ARSrc to the Address Bus, and set TmpAR to read.
1 | 0x10_00_00 | Write TmpAR to the Address Bus.
2 | 0x32_00_00 | Write TmpAR to the Address Bus, Address Bus Low register to the Data Bus, and set ARDest[L] to read from the Data Bus.
3 | 0x66_00_00 | Write Address Bus High Register to the Data Bus and set ARDest[H] to read from the Data Bus.
4 | 0x_00_00_80 | Advance PC.
80
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
MAA | Immediate (8-bit) |  | Immediate (8-bit) | ARDest | ARSrc[1] | OpCode=19 (and ARSrc[0] = 1)
19
MAA %DP, %BP, #-1
ARDest = ARSrc + Imm
INSTR[5] | INSTR[0] | ARSrc Address Register | Command Parameter
0 | 1 | DP | %DP
1 | 1 | BP | %BP

## Slide 81: Micro-Instructions Control: Move Address to General register (MAG) (11010)
Cycle # | Instruction | Explanation
0 | 0x00_00_00 | Write ARSrc to the Address Bus (special behavior due to opcode being MAG).
1 | 0x20_00_20 | Write Address Bus L/H Register to the Data Bus (L or H determined by the (AR) L/H instruction operand) and set Rd to read from the Data Bus.
2 | 0x00_00_80 | Advance PC.
81
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
MAG | XXXX |  | ARSrc | Rd | (AR) L/H | OpCode=1a
1A
MAG R3, %SP[L]
Rd = ARSrc[L/H]

## Slide 82: Micro-Instructions Control: Load Address register(LDA) (11011)
Cycle # | Instruction | Explanation
0 | 0x02_00_40 | Write Imm to the Data Bus and set ARDest[L/H] to read from the Data Bus.
1 | 0x00_00_80 | Advance PC.
82
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
LDA | Immediate (8-bit) |  |  | ARDest | (AR) L/H | OpCode=1b
1B
LDA %BP[L], #0x05
ARDest[L/H] = Imm

## Slide 83: Micro-Instructions Control: Move General to Address register (MGA) (11100)
Cycle # | Instruction | Explanation
0 | 0x02_00_10 | Write Rs1 to the Data Bus and set ARDest[L/H] to read from the Data Bus.
1 | 0x00_00_80 | Advance PC.
83
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
MGA | XX | Rs1 | X | ARDest | (AR) L/H | OpCode=1c
1C
MGA %SP[L], R2
ARDest[L/H] = Rs1

## Slide 84: 138 - 3-to-8 Line Decoder

## Slide 85: 161 - 4-Bit Binary Counter, Asynchronous Reset
Notes:
Parallel Load need to happen on invese clock
Count need to happen on [TBD – need timing diagram of the PC Advance]

## Slide 86: 175 - Quad D-Type Flip-Flop with Reset

## Slide 87: 245 - Octal D-Type Flip-Flop with Reset

## Slide 88: 273 - Octal D-Type Flip-Flop with Reset

## Slide 89: 547 - Octal 3−State Noninverting D Flip−Flop

## Slide 90: ByteFrost V1.0 – First Working Version

## Slide 91: Fetch State Machine Example
Program
(EEPROM)
Program
Counter
Address
Data
Instruction Register
Low
Micro Ins
(EEPROM)
Opcode
Micro Ins
Counter
Address Hi
Address Lo
Data
PC Advance
Fetch State Machine
Instruction Register
High
91

## Slide 92: Hardware
Register File
Clock
PC Advance
H Reg Out
Relative Branch
Load Flags
Load Flags
Load A and B
ALU MUX
ADC
SBC
XOR MUX
XOR
ADD SUB
SRAM
SRAM
Control
Reg Out
Select
Debug Mode
Status And Control
Branch
Load PC
Micro Intructions
Program Counter

## Slide 93: Register File
Read from Register
~G Output Enable
A,B Register Id
Write to Register
~G: Input Clock Enable
A,B Register Id
Clock
C1
C0
C2
C3
OE0
OE1
OE2
OE3
R3
R2
R1
R0
C3
C2
C0
C1
OE3
OE2
OE1
OE0
D1
D2
D3
D4
D5
D6
D7
D8
Main CLK
Read from Register
~G Output Enable
A,B Register Id
R.O. Select Low
R.O. Select High
HC139
µC 5. Reg In En
µC 4. Reg Out En
OpCode [7:6] Rd
OpCode
[7:6] Rd RI
93

## Slide 94: Registers Schematics
OE3
OE2
OE1
OE0
Read from Register
~G Output Enable
A,B Register Id
Write to Register
~G: Input Clock Enable
A,B Register Id
Clock
C2
C3
C0
C1
R.O. Select Low
R.O. Select High
Main CLK
µC 5. Reg In En
µC 4. Reg Out En
94
OpCode [7:6] Rd

## Slide 95: Register Out (RO) Select
74HC153
Dual
4:1 MUX
OpCode[12]: Rs1 Low
OpCode[15]: Rs2 High
OpCode[13]: Rs1 High
OpCode[14]: Rs2 Low
OpCode[6]: Rd Low
OpCode[7]: Rd High
R.O. Select Low
R.O. Select High
µC 3: Reg Out Select
µC 13: Reg Out Rd
OpCode
[7:6]
OpCode
[15:12]
95

## Slide 96: Clock
220
0.1uF
Or
10uF
100Ω
9.3kΩ
Parts | Min | Frequency
0.01uF (103) | 5KHz | 420KHz
R2=100 |  | 
Rpin5=10K |  | 
2
6
Single Step
(Yellow wire)
S.S. CLK
Running CLK
10KΩ
R on pin 5:
The design of using Vout as power for charging C1 generates 50% duty cycle only if Vout==Vcc. In reality, it is lower and the capacitor takes more time to reach the higher trigger point and duty cycle without it is only 33%.
With 10K on pin 5, both triggering points become lower, closer to 1/3 and 2/3 of Vout (instead of Vcc). That provides 50% duty cicle,also increase the frequency because the distance between the points is smaller (increasing the max frequency of this design from 250hHz to 420kHz)
96

## Slide 97: Clock Gating
74LS76
Running CLK
Op Code 1: BRK
Reset
BRK Button
(Purple)
Cont. Button
(Gray)
S.S. CLK
Running CLK
Reset
Main Reset
Main CLK
Reset LED
(Orange wire)
RUN LED
(Brown wire)
Halt LED
(Blue wire)
Clock LED
(Green wire)
Reset Button
(Red wire)
4ms
2s
Clock gating 2sec for
Arduino (display) to boot
97

## Slide 98: Micro Instructions EEPROMs
Counter A2..A0
Micro Ins 8_15
1,0,0,0,0,0,0,0
1,0,0,0,0,0,0,0
µC 7: PC Advance
µC 6: Out Reg H
µC 5. Reg In En
µC 4: Reg Out En
µC 3: Reg Out Select
µC 2: ALU Out En
µC 1: ALU Load A
µC 0: ALU Load B
µC 5. Reg In En
µC 4. Reg Out En
Micro Ins 0_7
5 bit
0,0
0,0
3 bit
3 bit
5 bit
Opcode A7..A3
µC 2. ALU Out En
µC 15: SP Count
µC 14: SP Addr
µC 13: Reg Out Rd
µC 12: Ld Data Addr
µC 11: RAM Store
µC 10: RAM Load
µC 9: PC Out
µC 8: PC Load
161
3 bit
Main CLK
# Reset_microPC
OpCode
[4:0]
Micro Ins 16_23
1,0,0,0,0,0,0,0
5 bit
0,0
3 bit
µC 23:
µC 22:
µC 21:
µC 20:
µC 19:
µC 18:
µC 17:
µC 16: SP Up/Down
98
Obsolete

## Slide 99: Program Counter
Program Address Bus
74HC161 [7:4]
74HC161 [3:0]
Data Bus
Main Reset
Main CLK
Load PC
INC Prog Counter
Prog EEPROM
Addr
[7:4]
Addr
[3:0]
Addr
[8:1]
Prog Counter Addr[0]
Addr
[7:0]
Prog
Data[7:0]
Addr
[7:0]
µC 9: PC Out
74HC245
99
Obsolete

## Slide 100: Fetch State Machine
MR
175
273 Hi
273 Lo
Reset_microPC Active Low
INC Prog Counter
Prog Counter lsb
Decimal
Dot LED
Main Reset
µC 7: PC Advance
Main CLK
Prog
Data[7:0]
Prog
Data[7:0]
OpCode
[4:0]
H Reg
8 bits
OpCode
[7:5] Flags
OpCode
[7:6] Rd RO
OpCode
[15:12]
OpCode
[7:6] Rd RI
OpCode [5] A/I
100
Obsolete

## Slide 101: Fetch State Machine
MR
175
273 Hi
273 Lo
Reset_microPC Active Low
INC Prog Counter
Prog Counter lsb
Decimal
Dot LED
Main Reset
µC 7: PC Advance
Main CLK
Prog
Data[7:0]
Prog
Data[7:0]
OpCode
[4:0]
H Reg
8 bits
OpCode
[7:5] Flags
OpCode
[7:6] Rd RO
OpCode
[15:12]
OpCode
[7:6] Rd RI
OpCode [5] A/I
101
1
1
0
1
Obsolete

## Slide 102: OpCode Decoder
74HC138
OpCodes 8-15
74HC138
OpCodes 0-7
74HC138
OpCodes 16-23
OpCode
[4:0]
0
1
2
3
4
OpCode_6
OpCode_08
OpCode_0D
Op Code 1: BRK
OpCode_7
BRANCH Relative
‘0’
‘0’
‘1’
102
Obsolete

## Slide 103: Output H Register to Data Bus
HC245
H  Bus
HC245
H4  Bus
Data
Bus
If opcode is 00110 or 10011, then msb-extended 4-bit immediate from high instruction register
is written to the bus; otherwise, the full 8-bit high instruction register is written to
bus as an 8-bit immediate
H Reg[7:4]
OpCode_13
µC 6: Out Reg H
H Reg
8 bits
103
OpCode_6

## Slide 104
ALU Interface – Flags, A,B Registers, Op Code selection
ALU
ALU OpCode
Flags
Carry In
74HC251
74HC161
Parallel Load Enable
74HC157
4b’0110 (ADD)
4b from H reg[3:0]
OpCode_7
BRANCH Relative
Gray
0
1
Don’t update flags on BR relative
MR
Clock
Clk
Clk
A_I
µC 2. ALU Out En
µC 1: ALU Load A
µC 0: ALU Load B
74HC161
74HC161
Data
Bus
Data Bus
74HC161
74HC161
A
B
C
Flags
Notes: Registers A and B are implemented by two HC161s, each stores 4 bits as the typical HC273 and HC347 won't fit into the 16pin sockets on the ALU wireup board.
The branch relative instruction doesn’t update flag bits to avoid corrupting the flag register state when executing a branch instruction (which may occur due to the ADD operation performed)

## Slide 105: Branch
74HC151
Flags
74HC161
‘1’
‘N’
‘C’
‘Z’
D4
D5
D6
D7
Q7 Q6 Q5
Instruction LSB
C2 | C1 | C0 | Condition | Instruction LSB | Equivalent Assembly Instruction
0 | 0 | 0 | JMP | 05 | JMP
0 | 0 | 1 | N | 25 | BMI – Branch on Minus
0 | 1 | 0 | C | 45 | BCS – Branch Carry Set
0 | 1 | 1 | Z | 65 | BEQ – Branch Equal
1 | 0 | 0 | Never | 85 | NOP
1 | 0 | 1 | !N | A5 | BPL – Branch on Plus
1 | 1 | 0 | !C | C5 | BCC – Branch Carry Clear
1 | 1 | 1 | !Z | E5 | BNE
Load PC
µC 8: PC Load
OpCode
[7:5]

## Slide 106: ALU OpCodes 2,3,7
ALU opcode(010), SF(0 / 1) – A XOR B / !B
No change to the source SF for ADD/SUB/ADC/SBC/!B
x8
SF
SF
ADD/SUB/ADC/SBC/!B
B or !B
A
8
8
B
Op Code ‘010’ output
Adder
A
Carry-in to Adder
Op Codes
‘011’ , ‘111’
{Op =XX0, SF = 0}  A XOR B; Else B or !B
ALU_Op[0]
0
1
x8
106
Op Select | Special Func. = 0 |  | Special Func. = 1 |  | Flag in
010 - 2 | A XOR B | XOR: 4 | !B | NOT: 5 | -
011 - 3 | A + B | ADD: 6 | A – B | SUB: 7 | -
111- 7 | A + B + Cin | ADC: E | A – B + Cin | SBC: F | Cin
!B or (A XOR B)

## Slide 107: ALU: ADD Carry/SUB Carry
Note the difference between the ALU function opcodes for ADD / SUB and ADC / SBC:
  ALU opcode(011), SF(0 / 1) – ADD/SUB
  ALU opcode(111), SF(0 / 1) – ADC/SBC
Note: The 6502 ISA only supports ADC/SBC (along with Set Carry and Reset Carry)
157
ALU_Op[2]
SF
ADD/SUB
Carry-in to Adder
Carry-in from last Op (from carry bit in flags register)
ADC/SBC
0
1
107

## Slide 108: SRAM (v1.0)
Data
Bus
374 Addr
I/O[0:7]
Q[1:8]  A[0:7]
Clock
!Clk
Control
AND
Clk
Main CLK
µC 12: Ld Data Addr
µC 11: RAM Store
µC 10: RAM Load
SRAM
169: Up Down Counter
µC 15: SP Count
µC 14: SP Addr
µC 16: SP Up/Down
3state
3state
MR
Load 0
Up/Down
245: 3-state
Count
Change MSB
108

## Slide 109: Display
Disp Char
5 4 3 2 1 0
6 7
MR
Display Load
OpCode [5] A/I
INT0

## Slide 110: Display Load
Display Load
µC 6: Out Reg H
µC 3: Reg Out Select
OpCode_08
OpCode_0D
Main CLK
273 Char
Data Bus
Disp Char

## Slide 111: Op Code & Micro Instruction
111
111

## Slide 112: Assembler Syntax
An assembly file is composed of lines with the following form:
[INSTR] [PARAM 1] [, PARAM 2] [, PARAM 3] // Comment
Misc. Instruction | Meaning | Format
NOP | No operation | NOP
BRK | Stop | BRK
OUT | Print 8-bit value to output | OUT Rs, #imm
ALU Instruction | Meaning | Format
OR | Bitwise OR | OR Rd, Rs1, Rs2
AND | Bitwise AND | AND Rd, Rs1, Rs2
XOR | Bitwise XOR | XOR Rd, Rs1, Rs2
NOT | Bitwise NOT | NOT Rd, Rs1
ADD | Addition | ADD Rd, Rs1, Rs2
SUB | 2’s Complement subtraction | SUB Rd1, Rs1, Rs2 (Rd1 = Rs1 – Rs2)
LSL | Bitwise logical shift left by 1 bit | LSL Rd, Rs1
ASR | Arithmetic shift right by 1 bit | ASR Rd, Rs1
ADC | Add with carry | ADC Rd, Rs1, Rs2
SUC | Subtract with borrow (using carry flag) | SUC Rd, Rs1, Rs2 (Rd1 = Rs1 – Rs2)
Register Instruction | Meaning | Format
LDR | Load register with 8-bit immediate | LDR Rd, #imm
MOV | Copy register value to another register | MOV Rd, Rs
Branch Instruction | Meaning | Format
JMP | Unconditional branch | A + I: JMP #imm A + R: R + I: R + R:
BIN | Branch If Negative | A + I: BIN #imm
BIC | Branch if Carry | A + I: BIC #imm
BIZ | Branch if Zero | A + I: BIZ #imm
BNN | Branch if not Negative | A + I: BNN #imm
BNC | Branch if not Carry | A + I: BNC #imm
BNZ | Branch if not Zero | A + I: BNZ #imm
112

## Slide 113: Instruction set families
Type | 0 1 2 3 4 | 5 | 6 7 | 8 9 10 11 | 12 13 | 14 15
ALU | OpCode | X | Rd | Function | Rs1 | Rs2
0 15
Type | 0 1 2 3 4 | 5 | 6 7 | 8 9 10 11 | 12 13 | 14 15
Load Imm | OpCode | X | Rd | Immediate (8-bit) | Rs1 | Rs2
Type | 0 1 2 3 4 | 5 | 6 7 | 8 9 10 11 | 12 13 | 14 15
Load Reg | OpCode | X | Rd | XXXX | Rs1 | XX
113

## Slide 114: Instruction set
Op code | Instruction | Details
0000 | NOP | No operation
0001 | BRK | Break
0010 | ALU (Format ALU Rd, Rs1, Rs2) | ALU instruction
0011 | LDR | Load Register (immediate, other register) ?
0100 | MOV | Copy Register (MOV instruction in ARM)
0101 | Branch Absolute | Jump to an address (8bit)
0110 | ALU Immediate (Format: ALU Rd, Rd, imm) | ALU instruction with value from immediate
0111 | BRANCH Relative | Relative Branch (+127 to -128)
1000 | OUT reg | Send a register as a character or integer to the display
1001 | LMA | Load register from address
1010 | SMA | Store register to address
1011 | LMR | Load register from address in another register
1100 | SMR | Store register into an address in another register
1101 | GSB | Jump, store current PC in stack
1110 | RTN | Load PC from stack
1111 | OUT Immediate | Send Reg H as a character or integer to display
Phase 0 | NOP, BRK
Phase 1 | Fib, Mult
Phase 2 | Self Test
Phase 3 | Display, 8 Queen
Completed | 
114

## Slide 115: Micro-Instructions Control: NOP Instruction (00000)
Cycle # | Instruction | Explanation
0 | 00000000 = 0x00 | 
1 | 10000000 = 0x80 | Increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
0
NOP
115
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 116: Micro-Instructions Control: BREAK (00001)
Cycle # | Instruction | Explanation
0 | 00000000 = 0x00 | Do nothing
1 | 10000000 = 0x80 | Increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
1
BRK
116
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Note: BRK has the same microcode as NOP, but the opcode decoder halts the clock when the opcode 00001 is detected. Stepping through it manually (via Single-Step / Run button press) resumes the clock. Hence, BRK acts as a hardware breakpoint.

## Slide 117: ALU with changes
Op Select | Special Func. = 0 |  | Special Func. = 1 |  | Flag in | Flags Out
0 | A OR B | OR: 0 | A OR B |  | - | Z, N
1 | A AND B | AND: 2 | A AND B |  | - | 
2 | A XOR B | XOR: 4 | ~B | NOT: 5 | - | Z, N
3 | A + B | ADD: 6 | A – B | SUB: 7 | - | Z, N, Co
4 | Shift Left A A[0]=0 | ASL: 8 | Rotate left A A[0]=Cin | ROL: 9 | Cin (Rotate) | Z, N=A[6], Co=A[7]
5 | Shift Right A | LSR: A | Arithmetic S.R. A | ASR: B | - | Z, N, Co=A[0]
6 | Rotate Right | ROR: C | Cin -> A-> Cout |  | Cin | Z, N, Co=A[0]
7 | A + B + Cin | ADC: E | A – B + Cin | SBC: F | Cin | Z, N, Co
Proposals for the additional operations
How to chain Shift Right of two bytes?
Proposal | # of IC slots | Description | Op Code
OR and ADD share Op Code (low priority) | 2x 74LS157 | Special Function select OR or AND | Release op code
Move A, B Regs (require replacement of 74LS251 with 74HC251) | 4x 74LS161 1x 74LS00 NAND | Reduce interface to one data bus instead of A, B, C (NAND for clock gate/invert) | No change
117

## Slide 118: Micro-Instructions Control: ALU (00010)
Cycle # | Instruction | Explanation
0 | 00010010 = 0x12 | Load Rs1 to reg A
1 | 00011001 = 0x19 | Load Rs2 to reg B
2 | 00100100 = 0x24 | Output and Read to Rd
3 | 10000000 = 0x80 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
ALU | Rs2 | Rs1 | S2 S1 S0 SF (Function sel) | Rd | XX | OpCode
2
ADD Rd, Rs1, Rs2
118
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 119: Micro-Instructions Control: Load Immediate to Reg (00011)
Cycle # | Instruction | Explanation
0 | 01100000 = 0x60 | Write imm to bus and Rd read
1 | 10000000 = 0x80 | Increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Imm | OpCode | XX | Rd | Immediate (8-bit) | Rs1 | Rs2
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Imm | Immediate (8-bit) |  | Immediate (8-bit) | Rd | X | OpCode
3
LDR Rd, #0x00
119
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 120: Micro-Instructions Control: MOV (00100)
Cycle # | Instruction | Explanation
0 | 00110000 = 0x30 | Write Rs1 to bus and Rd reads
1 | 10000000 = 0x80 | Increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Reg | OpCode | XX | Rd | XXXX | Rs1 | XX
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | XX | Rs1 | XXXX | Rd | X | OpCode
4
MOV Rd, Rs1
120
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 121: Micro-Instructions Control: Branch / Jump Absolute Immediate (00101)
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 5 | 4 3 2 1 0
Branch | Immediate (8-bit) |  | Immediate (8-bit) | C2 C1 C0 | OpCode
Cycle # | Instruction | Explanation
0 | 0x1_40 01_0100_0000 | Write H register to bus and PC (conditionally) reads
1 | 0x0_80 00_1000_0000 | PC advance
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
C2 | C1 | C0 | Condition | Low instruction register | Assembly
0 | 0 | 0 | JMP | 05 | JMP
0 | 0 | 1 | N | 25 | BMI – Branch on Minus
0 | 1 | 0 | C | 45 | BCS – Branch Carry Set
0 | 1 | 1 | Z | 65 | BEQ – Branch Equal
1 | 0 | 0 | Never | 85 | NOP
1 | 0 | 1 | !N | A5 | BPL – Branch on Plus
1 | 1 | 0 | !C | C5 | BCC – Branch Carry Clear
1 | 1 | 1 | !Z | E5 | BNE
5
121
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 122: Micro-Instructions Control: ALU immediate (4-bit) (00110)
Cycle # | Instruction | Explanation
0 | 10_0000_0001_0010 = 2012 | Load Rd to reg A
1 | 0100_0001 = 0x0041 | Load 4 bit imm to reg B
2 | 0010_0100 = 0x0024 | Write ALU output to Rd
3 | 1000_0000 = 0x0080 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
Type | 15 14 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
ALU | 4-bit imm. | S2 S1 S0 SF (Function sel) | Rd | X | OpCode
6
ADD Rd, #0x00
122
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 123: Micro-Instructions Control: Branch / Jump Relative Immediate (00111)
Cycle # | Instruction | Explanation
0 | 10_0000_0010 0x2_02 | Load PC into reg A
1 | 00_0100_0001 0x0_41 | Load immediate into reg B
2 | 01_0000_0100 0x1_04 | Output ALU val, load PC
3 | 00_1000_0000 0x0_80 | Advance PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
C2 | C1 | C0 | Condition | OpCode | Assembly
0 | 0 | 0 | JMP | 07 | JMP
0 | 0 | 1 | N | 27 | BMI – Branch on Minus
0 | 1 | 0 | C | 47 | BCS – Branch Carry Set
0 | 1 | 1 | Z | 67 | BEQ – Branch Equal
1 | 0 | 0 | Never | 87 | NOP
1 | 0 | 1 | !N | A7 | BPL – Branch on Plus
1 | 1 | 0 | !C | C7 | BCC – Branch Carry Clear
1 | 1 | 1 | !Z | E7 | BNE
7
123
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 5 | 4 3 2 1 0
Branch | Immediate (8-bit) |  | Immediate (8-bit) | C2 C1 C0 | OpCode

## Slide 124: Micro-Instructions Control: OUT (01000) (Display ASCII or Integer)
Cycle # | Instruction | Explanation
0 | 0000_0000 = 0x00 | Wait for H register to be loaded (need value of Rs1)
1 | 0001_0000 = 0x10 | Write Rs1 to the bus (when opcode 01000 is detected, the value on the bus is read by the OUT register to the display)
2 | 1000_0000 = 0x80 | Advance PC
3 |  | 
4 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Reg | OpCode | XX | Rd | XXXX | Rs1 | XX
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 | 3 2 1 0
Out | XX | Rs1 | XXXX | XX | I=1 A=0 | X | OpCode
8
OUT Rs1, A
124
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Out | XX | Rs1 | XXXX | XX | I=1 A=0 | OpCode

## Slide 125: Micro-Instructions Control: LMA (Load Memory Absolute) (01001)
Cycle # | Instruction | Explanation
0 | 1_0000_0100_0000 = 1040 | Load 8-bit address to address register
1 | 0_0100_0010_0000 = 0420 | Read byte from RAM and store in Rd
2 | 0_0000_1000_0000 = 0080 | Increment PC
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
9
Type | 15 14 13 12 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | 8-bit (LSBs) Address | Rd | X | OpCode
LMA Rd, #Addr
125
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 126: Micro-Instructions Control: SMA (Store Memory Absolute) (01010)
Cycle # | Instruction | Explanation
0 | 01_0000_0100_0000 = 1040 | Load 8-bit address to address register
1 | 10_1000_0001_0000 = 2810 | Store byte to RAM from Rd
2 | 00_0000_1000_0000 = 0080 | Increment PC
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
A
Type | 15 14 13 12 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | 8-bit (LSBs) Address | Rd | X | OpCode
SMA Rd, #Addr
126
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 127: Micro-Instructions Control: LMR (Load Memory Register) (01011)
Cycle # | Instruction | Explanation
0 | 1_0000_0001_0000 = 1010 | Load Rs1 to Address Register
1 | 0_0100_0010_0000 = 0420 | Load value at the address into Rd
2 | 0_0000_1000_0000 = 0080 | Increment PC
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | XX | Rs1 | XXXX | Rd | X | OpCode
LMR Rd, Rs
127
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Effect: Rd = *Rs

## Slide 128: Micro-Instructions Control: SMR (Store Memory Register) (01100)
Cycle # | Instruction | Explanation
0 | 01_0000_0001_0000 = 1010 | Load Rs1 to Address Register
1 | 10_1000_0001_0000 = 2810 | Store value at Rd to RAM
2 | 00_0000_1000_0000 = 0080 | Increment PC
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
C
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | XX | Rs1 | XXXX | Rd | X | OpCode
SMR Rd_data, Rs1_addr
128
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 129: Micro-Instructions Control: OUT immediate (01101)
Cycle # | Instruction | Explanation
0 | 0000_0000 = 0x00 | Wait for H instruction register to be loaded
1 | 0100_0000 = 0x40 | Write program register H to the bus
2 | 1000_0000 = 0x80 | Advance PC
3 |  | 
4 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Reg | OpCode | XX | Rd | XXXX | Rs1 | XX
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 | 3 2 1 0
Out | 8-bit immediate |  | XXXX | XX | I=1 A=0 | X | OpCode
D
OUT Rs1, A
129
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Out | 8-bit immediate |  | XXXX | XX | I=1 A=0 | OpCode

## Slide 130: Micro-Instructions Control: PUSH (01110)
Cycle # | Instruction | Explanation
0 | 0_0100_1000_0001_0000 = 0x04810 | Store Rs1 in the stack
1 | 1_1000_0000_1000_0000 = 0x18080 | Increment stack pointer (and increment PC)
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
E
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | XX | Rs1 | XXXX | XX | X | OpCode
PUSH Rs1
130
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 131: Micro-Instructions Control: POP (1111)
Cycle # | Instruction | Explanation
0 | 0_0000_0000_0000_0000 = 0x00000 | Wait for next clock
1 | 0_1000_0000_0000_0000 = 0x08000 | Decrement stack pointer
2 | 0_0100_0100_0010_0000 = 0x04420 | Load value from stack to Rd
3 | 0_0000_0000_1000_0000 = 0x00080 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
F
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Reg | XX | XX | XXXX | Rd | X X | OpCode
POP Rd
131
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 132: Micro-Instructions Control: JSR Jump Subroutine (10000)
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 0_0100_1010_0000_0000 = 0x04A00 | Write PC to stack
1 | 1_1000_0000_0000_0000 = 0x18000 | Increase stack pointer
2 | 0_0000_0001_0100_0000 = 0x00140 | Jump to immediate address
3 | 0_0000_0000_1000_0000 = 0x00080 | Advance PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
10
Type | 15 14 13 12 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Reg | 8-bit Immediate (Program Address) | XX | X X | OpCode
JSR #Imm
132

## Slide 133: Micro-Instructions Control: RTS Return from Subroutine (10001)
Cycle # | Instruction | Explanation
0 | 0_0000_0000_0000_0000 = 0x00000 | Wait a clock cycle
1 | 0_1000_0000_0000_0000 = 0x08000 | Decrement stack pointer
2 | 0_0100_0101_0000_0000 = 0x04500 | Load program address on the stack to the program counter
3 | 0_0000_0000_1000_0000 = 0x00080 | Advance PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
11
Type | 15 14 13 12 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Reg | XXXX XXXX | XX | X X | OpCode
RTS
133
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 134: Micro-Instructions Control: Test (10010)
Cycle # | Instruction | Explanation
0 | 0001_0010 = 0x12 | Load Rs1 to reg A
1 | 0001_1001 = 0x19 | Load Rs2 to reg B
2 | 0000_0100 = 0x04 | Output ALU value on bus (but don’t save in register)
3 | 1000_0000 = 0x80 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
ALU | Rs2 | Rs1 | S2 S1 S0 SF (Function sel) | Rd | XX | OpCode
TST Rs1, Rs2
12
134
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 135: Micro-Instructions Control: Test immediate (10011)
Cycle # | Instruction | Explanation
0 | 10_0000_0001_0010 = 0x2012 | Load Rd to reg A
1 | 0100_0001 = 0x0041 | Load 4 bit imm to reg B
2 | 0000_0100 = 0x0004 | Write ALU output to bus (but not to register)
3 | 1000_0000 = 0x80 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
Type | 15 14 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
ALU | 4-bit imm. | S2 S1 S0 SF (Function sel) | Rd | XX | OpCode
TST Rd, #0x00
13
135
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 136: ALU
Op Select | Special Func. = 0 | Special Func. = 1 | Flag in | Flags Out
0 | A OR B | A OR B | - | Z, N
1 | A AND B | A AND B | - | Z, N
2 | B | ~B | - | Z, N
3 | A + B | A – B | - | Z, N, Co
4 | Shift Left A A[0]=0 | Rotate left A A[0]=Cin | Cin (Rotate) | Z, N=A[6], Co=A[7]
5 | Shift Right A | Arithmetic S.R. A | - | Z, N, Co=A[0]
6 |  |  |  | 
7 |  |  |  | 
Proposals for the additional operations
How to chain Shift Right of two bytes?
Proposal | # of IC slots | Description | Op Code
Move A, B Regs | 4x 74LS161 | Reduce interface to one data bus instead of three (A, B, C) | No change
136

## Slide 137: And the Name …

## Slide 141
ByteFrost