## Slide 1: And the Name …

## Slide 2
ByteFrost

## Slide 3: Hardware
Register File
Clock
PC Advance
H Reg Out
Relative Branch
Load Flags
Load Flags
Load A and B
ALU MUX
ADC
SBC
XOR MUX
XOR
ADD SUB
SRAM
SRAM
Control
Reg Out
Select
Debug Mode
Status And Control
Branch
Load PC
Micro Intructions
Program Counter

## Slide 4
Program
(EEPROM)
Program
Counter
Address
Data
Instruction Register
Low
Micro Ins
(EEPROM)
Opcode
Micro Ins
Counter
Address Hi
Address Lo
Data
PC Advance
State Machine
Instruction Register
High

## Slide 5: Register File
Read from Register
~G Output Enable
A,B Register Id
Write to Register
~G: Input Clock Enable
A,B Register Id
Clock
C1
C0
C2
C3
OE0
OE1
OE2
OE3
R3
R2
R1
R0
C3
C2
C0
C1
OE3
OE2
OE1
OE0
D1
D2
D3
D4
D5
D6
D7
D8
Main CLK
Read from Register
~G Output Enable
A,B Register Id
R.O. Select Low
R.O. Select High
HC139
µC 5. Reg In En
µC 4. Reg Out En
OpCode [7:6] Rd
OpCode
[7:6] Rd RI

## Slide 6: Registers Schematics
OE3
OE2
OE1
OE0
Read from Register
~G Output Enable
A,B Register Id
Write to Register
~G: Input Clock Enable
A,B Register Id
Clock
C2
C3
C0
C1
R.O. Select Low
R.O. Select High
Main CLK
µC 5. Reg In En
µC 4. Reg Out En
6

## Slide 7
Register Out (RO) Select
74HC153
Dual
4:1 MUX
OpCode[12]: Rs1 Low
OpCode[15]: Rs2 High
OpCode[13]: Rs1 High
OpCode[14]: Rs2 Low
OpCode[6]: Rd Low
OpCode[7]: Rd High
R.O. Select Low
R.O. Select High
µC 3: Reg Out Select
µC 13: Reg Out Rd
OpCode
[7:6]
OpCode
[15:12]
7

## Slide 8: Clock
220
0.1uF
Or
10uF
100Ω
9.3kΩ
Parts | Min | Frequency
0.01uF (103) | 5KHz | 420KHz
R2=100 |  | 
Rpin5=10K |  | 
2
6
Single Step
(Yellow wire)
S.S. CLK
Running CLK
10KΩ
R on pin 5:
The design of using Vout as power for charging C1 generates 50% duty cycle only if Vout==Vcc. In reality, it is lower and the capacitor takes more time to reach the higher trigger point and duty cycle without it is only 33%.
With 10K on pin 5, both triggering points become lower, closer to 1/3 and 2/3 of Vout (instead of Vcc). That provides 50% duty cicle,also increase the frequency because the distance between the points is smaller (increasing the max frequency of this design from 250hHz to 420kHz)
8

## Slide 9
Clock Gating
74LS76
Running CLK
Op Code 1: BRK
Reset
BRK Button
(Purple)
Cont. Button
(Gray)
S.S. CLK
Running CLK
Reset
Main Reset
Main CLK
Reset LED
(Orange wire)
RUN LED
(Brown wire)
Halt LED
(Blue wire)
Clock LED
(Green wire)
Reset Button
(Red wire)
4ms
2s
Clock gating 2sec for
Arduino to boot

## Slide 10: Micro Instructions
Counter A2..A0
Micro Ins 8_15
1,0,0,0,0,0,0,0
1,0,0,0,0,0,0,0
µC 7: PC Advance
µC 6: Out Reg H
µC 5. Reg In En
µC 4: Reg Out En
µC 3: Reg Out Select
µC 2: ALU Out En
µC 1: ALU Load A
µC 0: ALU Load B
µC 5. Reg In En
µC 4. Reg Out En
Micro Ins 0_7
5 bit
0,0
0,0
3 bit
3 bit
5 bit
Opcode A7..A3
µC 2. ALU Out En
µC 15: SP Count
µC 14: SP Addr
µC 13: Reg Out Rd
µC 12: Ld Data Addr
µC 11: RAM Store
µC 10: RAM Load
µC 9: PC Out
µC 8: PC Load
161
3 bit
Main CLK
Reset_microPC Active Low
OpCode
[4:0]
Micro Ins 16_23
1,0,0,0,0,0,0,0
5 bit
0,0
3 bit
µC 23:
µC 22:
µC 21:
µC 20:
µC 19:
µC 18:
µC 17:
µC 16: SP Up/Down

## Slide 11: Program Counter
Program Address Bus
74HC161 [7:4]
74HC161 [3:0]
Data Bus
Main Reset
Main CLK
Load PC
INC Prog Counter
Prog EEPROM
Addr
[7:4]
Addr
[3:0]
Addr
[8:1]
Prog Counter Addr[0]
Addr
[7:0]
Prog
Data[7:0]
Addr
[7:0]
µC 9: PC Out
74HC245

## Slide 12
MR
Program Counter Advance
175
273 Hi
273 Lo
Reset_microPC Active Low
INC Prog Counter
Prog Counter lsb
Decimal
Dot LED
Main Reset
µC 7: PC Advance
Main CLK
Prog
Data[7:0]
Prog
Data[7:0]
OpCode
[4:0]
H Reg
8 bits
OpCode
[7:5] Flags
OpCode
[7:6] Rd RO
OpCode
[15:12]
OpCode
[7:6] Rd RI
OpCode [5] A/I
12

## Slide 13
MR
Program Counter Advance
175
273 Hi
273 Lo
Reset_microPC Active Low
INC Prog Counter
Prog Counter lsb
Decimal
Dot LED
Main Reset
µC 7: PC Advance
Main CLK
Prog
Data[7:0]
Prog
Data[7:0]
OpCode
[4:0]
H Reg
8 bits
OpCode
[7:5] Flags
OpCode
[7:6] Rd RO
OpCode
[15:12]
OpCode
[7:6] Rd RI
OpCode [5] A/I
13
1
1
0
1

## Slide 14: OpCode Decoder
74HC138
OpCodes 8-15
74HC138
OpCodes 0-7
74HC138
OpCodes 16-23
OpCode
[4:0]
0
1
2
3
4
OpCode_6
OpCode_08
OpCode_0D
Op Code 1: BRK
OpCode_7
BRANCH Relative
‘0’
‘0’
‘1’

## Slide 15
Output H Register to Bus
HC245
H  Bus
HC245
H4  Bus
Data
Bus
H4 format is used if OpCode is ‘0110’
Otherwise, use Full H format
H Reg[7:4]
OpCode_6
µC 6: Out Reg H
H Reg
8 bits
4b0

## Slide 16
ALU Interface – Flags, A,B Registers, Op Code selection
ALU
ALU OpCode
Flags
Carry In
74HC251
74HC161
Parallel Load Enable
74HC157
4b’0110 (ADD)
4b from H reg[3:0]
OpCode_7
BRANCH Relative
Gray
0
1
Don’t update flags on BR relative
MR
Clock
Clk
Clk
A_I
µC 2. ALU Out En
µC 1: ALU Load A
µC 0: ALU Load B
74HC161
74HC161
Data
Bus
Data Bus
74HC161
74HC161
A
B
C
Flags

## Slide 17: Branch
74HC151
Flags
74HC161
‘1’
‘N’
‘C’
‘Z’
D4
D5
D6
D7
Q7 Q6 Q5
OpCode Low Byte
C2 | C1 | C0 | Condition | OpCode | Assembly
0 | 0 | 0 | JMP | 05 | JMP
0 | 0 | 1 | N | 25 | BMI – Branch on Minus
0 | 1 | 0 | C | 45 | BCS – Branch Carry Set
0 | 1 | 1 | Z | 65 | BEQ – Branch Equal
1 | 0 | 0 | Never | 85 | NOP
1 | 0 | 1 | !N | A5 | BPL – Branch on Plus
1 | 1 | 0 | !C | C5 | BCC – Branch Carry Clear
1 | 1 | 1 | !Z | E5 | BNE
Load PC
µC 8: PC Load
OpCode
[7:5]

## Slide 18: ALU: ADD Carry/SUB Carry
011x – ADD/SUB
111x – ADC/SBC
Note 6502 only supports ADC/SBC (along with Set carry, Reset Carry)
157
ALU_Op[2]
SF
ADD/SUB
Carry-in to Adder
Carry-in from last Op
ADC/SBC
0
1
Adder
A
Both
‘011’ output
‘111’ output
B

## Slide 19: ALU: Not B/ A XOR B
010 – XOR / !B
No change to the source SF for ADD/SUB/ADC/SBC/!B
x8
SF
SF
ADD/SUB/ADC/SBC/!B
B’ to Adder
A
A XOR B
8
8
B
Op Code ‘010’ output
Adder
A
Carry-in to Adder
Op Code
‘011’ output
Op =XX0, SF = 0
ALU_Op[0]
0
1
x8
19

## Slide 20
SRAM
Data
Bus
374 Addr
I/O[0:7]
Q[1:8]  A[0:7]
Clock
!Clk
Control
AND
Clk
Main CLK
µC 12: Ld Data Addr
µC 11: RAM Store
µC 10: RAM Load
SRAM
169: Up Down Counter
µC 15: SP Count
µC 14: SP Addr
µC 16: SP Up/Down
3state
3state
MR
Load 0
Up/Down
245: 3-state
Count
Change MSB

## Slide 21: Display
Disp Char
5 4 3 2 1 0
6 7
MR
Display Load
OpCode [5] A/I
INT0

## Slide 22: Display Load
Display Load
µC 6: Out Reg H
µC 3: Reg Out Select
OpCode_08
OpCode_0D
Main CLK
273 Char
Data Bus
Disp Char

## Slide 23: Op Code & Micro Instruction

## Slide 24
Assembler Syntax
An assembly file is composed of lines with the following form:
[INSTR] [PARAM 1] [, PARAM 2] [, PARAM 3] // Comment
Misc. Instruction | Meaning | Format
NOP | No operation | NOP
BRK | Stop | BRK
OUT | Print 8-bit value to output | OUT Rs, #imm
ALU Instruction | Meaning | Format
OR | Bitwise OR | OR Rd, Rs1, Rs2
AND | Bitwise AND | AND Rd, Rs1, Rs2
XOR | Bitwise XOR | XOR Rd, Rs1, Rs2
NOT | Bitwise NOT | NOT Rd, Rs1
ADD | Addition | ADD Rd, Rs1, Rs2
SUB | 2’s Complement subtraction | SUB Rd1, Rs1, Rs2 (Rd1 = Rs1 – Rs2)
LSL | Bitwise logical shift left by 1 bit | LSL Rd, Rs1
ASR | Arithmetic shift right by 1 bit | ASR Rd, Rs1
ADC | Add with carry | ADC Rd, Rs1, Rs2
SUC | Subtract with borrow (using carry flag) | SUC Rd, Rs1, Rs2 (Rd1 = Rs1 – Rs2)
Register Instruction | Meaning | Format
LDR | Load register with 8-bit immediate | LDR Rd, #imm
MOV | Copy register value to another register | MOV Rd, Rs
Branch Instruction | Meaning | Format
JMP | Unconditional branch | A + I: JMP #imm A + R: R + I: R + R:
BIN | Branch If Negative | A + I: BIN #imm
BIC | Branch if Carry | A + I: BIC #imm
BIZ | Branch if Zero | A + I: BIZ #imm
BNN | Branch if not Negative | A + I: BNN #imm
BNC | Branch if not Carry | A + I: BNC #imm
BNZ | Branch if not Zero | A + I: BNZ #imm

## Slide 25
Instruction set families
Type | 0 1 2 3 | 4 5 | 6 7 | 8 9 10 11 | 12 13 | 14 15
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
0 15
Type | 0 1 2 3 | 4 5 | 6 7 | 8 9 10 11 | 12 13 | 14 15
Load Imm | OpCode | XX | Rd | Immediate (8-bit) | Rs1 | Rs2
Type | 0 1 2 3 | 4 5 | 6 7 | 8 9 10 11 | 12 13 | 14 15
Load Reg | OpCode | XX | Rd | XXXX | Rs1 | XX

## Slide 26
Instruction set
Op code | Instruction | Details
0000 | NOP | No operation
0001 | BRK | Break
0010 | ALU (Format ALU Rd, Rs1, Rs2) | ALU instruction
0011 | LDR | Load Register (immediate, other register) ?
0100 | MOV | Copy Register (MOV instruction in ARM)
0101 | Branch Absolute | Jump to an address (8bit)
0110 | ALU Immediate (Format: ALU Rd, Rd, imm) | ALU instruction with value from immediate
0111 | BRANCH Relative | Relative Branch (+127 to -128)
1000 | OUT reg | Send a register as a character or integer to the display
1001 | LMA | Load register from address
1010 | SMA | Store register to address
1011 | LMR | Load register from address in another register
1100 | SMR | Store register into an address in another register
1101 | GSB | Jump, store current PC in stack
1110 | RTN | Load PC from stack
1111 | OUT Immediate | Send Reg H as a character or integer to display
Phase 0 | NOP, BRK
Phase 1 | Fib, Mult
Phase 2 | Self Test
Phase 3 | Display, 8 Queen
Completed | 

## Slide 27
Micro-Instructions Control: NOP Instruction (0000)
Bit | Operation
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 00000000 = 0x00 | 
1 | 10000000 = 0x80 | Increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
0
NOP

## Slide 28
Micro-Instructions Control: BREAK (0001)
Bit | Operation
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 00000000 = 0x00 | Do nothing
1 | 00000000 = 0x00 | 
2 | 00000000 = 0x00 | 
3 | 00000000 = 0x00 | 
4 | 00000000 = 0x00 | 
5 | 00000000 = 0x00 | 
6 | 00000000 = 0x00 | 
7 | 00000000 = 0x00 | 
1
BRK

## Slide 29: ALU with changes
Op Select | Special Func. = 0 |  | Special Func. = 1 |  | Flag in | Flags Out
0 | A OR B | OR: 0 | A OR B |  | - | Z, N
1 | A AND B | AND: 2 | A AND B |  | - | 
2 | A XOR B | XOR: 4 | ~B | NOT: 5 | - | Z, N
3 | A + B | ADD: 6 | A – B | SUB: 7 | - | Z, N, Co
4 | Shift Left A A[0]=0 | ASL: 8 | Rotate left A A[0]=Cin | ROL: 9 | Cin (Rotate) | Z, N=A[6], Co=A[7]
5 | Shift Right A | LSR: A | Arithmetic S.R. A | ASR: B | - | Z, N, Co=A[0]
6 | Rotate Right | ROR: C | Cin -> A-> Cout |  | Cin | Z, N, Co=A[0]
7 | A + B + Cin | ADC: E | A – B + Cin | SBC: F | Cin | Z, N, Co
Proposals for the additional operations
How to chain Shift Right of two bytes?
Proposal | # of IC slots | Description | Op Code
OR and ADD share Op Code (low priority) | 2x 74LS157 | Special Function select OR or AND | Release op code
Move A, B Regs (require replacement of 74LS251 with 74HC251) | 4x 74LS161 1x 74LS00 NAND | Reduce interface to one data bus instead of A, B, C (NAND for clock gate/invert) | No change

## Slide 30
Micro-Instructions Control: ALU (0010)
Bit | Operation
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 00010010 = 0x12 | Load Rs1 to reg A
1 | 00011001 = 0x19 | Load Rs2 to reg B
2 | 10100100 = 0xA4 | Output and Read to Rd (and increment PC)
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
15 0
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
ALU | Rs2 | Rs1 | S2 S1 S0 SF (Function sel) | Rd | XX | OpCode
2
UPDATE THIS SO THAT RS1 goes to reg B and RS2 goes to regA (more intuitive way to write this(?))
ADD Rd, Rs1, Rs2

## Slide 31
Micro-Instructions Control: Load Immediate to Reg (0011)
Bit | Operation
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 01100000 = 0x60 | Write imm to bus and Rd reads (and increment PC)
1 | 10000000 = 0x80 | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Imm | OpCode | XX | Rd | Immediate (8-bit) | Rs1 | Rs2
15 0
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Imm | Immediate (8-bit) |  | Immediate (8-bit) | Rd | XX | OpCode
3
LDR Rd, #0x00

## Slide 32
Micro-Instructions Control: MOV (0100)
Bit | Operation
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 00110000 = 0x30 | Write Rs1 to bus and Rd reads (and increment PC)
1 | 10000000 = 0x80 | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Reg | OpCode | XX | Rd | XXXX | Rs1 | XX
15 0
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Reg | XX | Rs1 | XXXX | Rd | XX | OpCode
4
MOV Rd, Rs1

## Slide 33
Micro-Instructions Control: Branch / Jump Absolute Immediate (0101)
Bit | Operation
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 0x1_40 01_0100_0000 | Write H register to bus and PC (conditionally) reads
1 | 0x0_80 00_1000_0000 | PC advance
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Imm | OpCode | XX | Rd | Immediate (8-bit) | Rs1 | Rs2
15 0
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 5 | 4 | 3 2 1 0
Branch | Immediate (8-bit) |  | Immediate (8-bit) | C2 C1 C0 | X | OpCode
C2 | C1 | C0 | Condition | OpCode | Assembly
0 | 0 | 0 | JMP | 05 | JMP
0 | 0 | 1 | N | 25 | BMI – Branch on Minus
0 | 1 | 0 | C | 45 | BCS – Branch Carry Set
0 | 1 | 1 | Z | 65 | BEQ – Branch Equal
1 | 0 | 0 | Never | 85 | NOP
1 | 0 | 1 | !N | A5 | BPL – Branch on Plus
1 | 1 | 0 | !C | C5 | BCC – Branch Carry Clear
1 | 1 | 1 | !Z | E5 | BNE
5

## Slide 34
Micro-Instructions Control: ALU immediate (4-bit) (0110)
Cycle # | Instruction | Explanation
0 | 10_0000_0001_0010 = 2012 | Load Rd to reg A
1 | 0100_0001 = 0x0041 | Load 4 bit imm to reg B
2 | 1010_0100 = 0x00A4 | Write ALU output to Rd and increment PC
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
15 0
Type | 15 14 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
ALU | 4-bit imm. | S2 S1 S0 SF (Function sel) | Rd | XX | OpCode
6
Bit | Operation
13 | Use Rd as Source
12 | Lower Address Register Load
11 | RAM Store
10 | RAM Load
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
ADD Rd, #0x00

## Slide 35
Micro-Instructions Control: Branch / Jump Relative Immediate (0111)
Bit | Operation
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 10_0000_0010 0x2_02 | Load PC into reg A
1 | 00_0100_0001 0x0_41 | Load immediate into reg B
2 | 01_0000_0100 0x1_04 | Output ALU val, load PC
3 | 00_1000_0000 0x0_80 | Advance PC (if didn’t branch)
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Imm | OpCode | XX | Rd | Immediate (8-bit) | Rs1 | Rs2
15 0
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 5 | 4 | 3 2 1 0
Branch | Immediate (8-bit) |  | Immediate (8-bit) | C2 C1 C0 | X | OpCode
C2 | C1 | C0 | Condition | OpCode | Assembly
0 | 0 | 0 | JMP | 07 | JMP
0 | 0 | 1 | N | 27 | BMI – Branch on Minus
0 | 1 | 0 | C | 47 | BCS – Branch Carry Set
0 | 1 | 1 | Z | 67 | BEQ – Branch Equal
1 | 0 | 0 | Never | 87 | NOP
1 | 0 | 1 | !N | A7 | BPL – Branch on Plus
1 | 1 | 0 | !C | C7 | BCC – Branch Carry Clear
1 | 1 | 1 | !Z | E7 | BNE
7

## Slide 36
Micro-Instructions Control: OUT (1000) (Display ASCII or Integer)
Bit | Operation
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 0001_0000 = 0x10 | Write Rs1 to the bus (while output reg is reading (FPGA load signal is OPCODE MSB AND RF Out Enable))
1 | 1000_0000 = 0x80 | Advance PC
2 |  | 
3 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Reg | OpCode | XX | Rd | XXXX | Rs1 | XX
15 0
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 | 3 2 1 0
Out | XX | Rs1 | XXXX | XX | I=1 A=0 | X | OpCode
8
OUT Rs1, A

## Slide 37
Micro-Instructions Control: LMA (Load Memory Absolute) (1001)
Bit | Operation
12 | Lower Address Register Load
11 | RAM Store
10 | RAM Load
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 1_0000_0100_0000 = 1040 | Load 8-bit address to address register
1 | 0_0100_1010_0000 = 04A0 | Read byte from RAM and store in Rd (and increment PC)
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
15 0
9
Type | 15 14 13 12 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Reg | 8-bit (LSBs) Address | Rd | X X | OpCode
LMA Rd, #Addr

## Slide 38
Micro-Instructions Control: SMA (Store Memory Absolute) (1010)
Cycle # | Instruction | Explanation
0 | 01_0000_0100_0000 = 1040 | Load 8-bit address to address register
1 | 10_1000_1001_0000 = 2890 | Store byte to RAM from Rd and increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
A
Type | 15 14 13 12 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Reg | 8-bit (LSBs) Address | Rd | X X | OpCode
Bit | Operation
13 | Use Rd as Source
12 | Lower Address Register Load
11 | RAM Store
10 | RAM Load
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
SMA Rd, #Addr

## Slide 39
Micro-Instructions Control: LMR (Load Memory Register) (1011)
Bit | Operation
12 | Lower Address Register Load
11 | RAM Store
10 | RAM Load
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 1_0000_0001_0000 = 1010 | Load Rs1 to Address Register
1 | 0_0100_1010_0000 = 04A0 | Load value at the address into Rd and advance PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
15 0
B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Reg | XX | Rs1 | XXXX | Rd | X X | OpCode
LMR Rd, Rs

## Slide 40
Micro-Instructions Control: SMR (Store Memory Register) (1100)
Bit | Operation
13 | Use Rd as Source
12 | Lower Address Register Load
11 | RAM Store
10 | RAM Load
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 01_0000_0001_0000 = 1010 | Load Rs1 to Address Register
1 | 10_1000_1001_0000 = 2890 | Store value at Rd to RAM and increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
15 0
C
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Reg | XX | Rs1 | XXXX | Rd | X X | OpCode
SMR Rd_data, Rs1_addr

## Slide 41
Micro-Instructions Control: OUT immediate (1101)
Bit | Operation
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 0100_0000 = 0x40 | Write program register H to the bus
1 | 1000_0000 = 0x80 | Advance PC
2 |  | 
3 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Reg | OpCode | XX | Rd | XXXX | Rs1 | XX
15 0
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 | 3 2 1 0
Out | 8-bit immediate |  | XXXX | XX | I=1 A=0 | X | OpCode
D
OUT Rs1, A

## Slide 42
Micro-Instructions Control: PUSH (1110)
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | RAM Store
10 | RAM Load
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 0_0100_1000_0001_0000 = 0x04810 | Store Rs1 in the stack
1 | 1_1000_0000_1000_0000 = 0x18080 | Increment stack pointer (and increment PC)
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
15 0
E
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Reg | XX | Rs1 | XXXX | XX | X X | OpCode
PUSH Rs1

## Slide 43
Micro-Instructions Control: POP (1111)
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | RAM Store
10 | RAM Load
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 0_0000_0000_0000_0000 = 0x00000 | Wait for next clock
1 | 0_1000_0000_0000_0000 = 0x08000 | Decrement stack pointer
2 | 0_0100_0100_1010_0000 = 0x044A0 | Load value from stack to Rd (and increment program counter)
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
15 0
F
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Reg | XX | XX | XXXX | Rd | X X | OpCode
POP Rd

## Slide 44
Micro-Instructions Control: JSR Jump Subroutine (10000)
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | RAM Store
10 | RAM Load
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 0_0100_1010_0000_0000 = 0x04A00 | Write PC to stack
1 | 1_1000_0000_0000_0000 = 0x18000 | Increase stack pointer
2 | 0_0000_0001_0100_0000 = 0x00140 | Jump to immediate address
3 | 0_0000_0000_1000_0000 = 0x00080 | Advance PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
15 0
10
Type | 15 14 13 12 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Reg | 8-bit Immediate (Program Address) | XX | X X | OpCode
JSR #Imm

## Slide 45
Micro-Instructions Control: RTS Return from Subroutine (10001)
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | RAM Store
10 | RAM Load
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 0_0000_0000_0000_0000 = 0x00000 | Wait a clock cycle
1 | 0_1000_0000_0000_0000 = 0x08000 | Decrement stack pointer
2 | 0_0100_0101_0000_0000 = 0x04500 | Load program address on the stack to the program counter
3 | 0_0000_0000_1000_0000 = 0x00080 | Advance PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
15 0
11
Type | 15 14 13 12 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
Load Reg | XXXX XXXX | XX | X X | OpCode
RTS

## Slide 46
Micro-Instructions Control: Test (10010)
Bit | Operation
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Cycle # | Instruction | Explanation
0 | 0001_0010 = 0x12 | Load Rs1 to reg A
1 | 0001_1001 = 0x19 | Load Rs2 to reg B
2 | 1000_0100 = 0x84 | Output ALU value on bus (but don’t save in register) and increment PC
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
15 0
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
ALU | Rs2 | Rs1 | S2 S1 S0 SF (Function sel) | Rd | XX | OpCode
TST Rs1, Rs2
12

## Slide 47
Micro-Instructions Control: Test immediate (10011)
Cycle # | Instruction | Explanation
0 | 10_0000_0001_0010 = 0x2012 | Load Rd to reg A
1 | 0100_0001 = 0x0041 | Load 4 bit imm to reg B
2 | 1010_0100 = 0x0084 | Write ALU output to bus (but not to register) and increment PC
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
15 0
Type | 15 14 13 12 | 11 10 9 8 | 7 6 | 5 4 | 3 2 1 0
ALU | 4-bit imm. | S2 S1 S0 SF (Function sel) | Rd | XX | OpCode
Bit | Operation
13 | Use Rd as Source
12 | Lower Address Register Load
11 | RAM Store
10 | RAM Load
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
TST Rd, #0x00
13

## Slide 48: ALU
Op Select | Special Func. = 0 | Special Func. = 1 | Flag in | Flags Out
0 | A OR B | A OR B | - | Z, N
1 | A AND B | A AND B | - | Z, N
2 | B | ~B | - | Z, N
3 | A + B | A – B | - | Z, N, Co
4 | Shift Left A A[0]=0 | Rotate left A A[0]=Cin | Cin (Rotate) | Z, N=A[6], Co=A[7]
5 | Shift Right A | Arithmetic S.R. A | - | Z, N, Co=A[0]
6 |  |  |  | 
7 |  |  |  | 
Proposals for the additional operations
How to chain Shift Right of two bytes?
Proposal | # of IC slots | Description | Op Code
Move A, B Regs | 4x 74LS161 | Reduce interface to one data bus instead of three (A, B, C) | No change

## Slide 49: And the Name …

## Slide 53
ByteFrost