## Slide 1
Byte Frost
V3.0 PCB

## Slide 2: ByteFrost V3.0 – Migration to PCB
While most of the design is kept from v2.0, the migration to
Backplane and distributed PCB boards impact every circuit.
In addition, all the schematics are real, and not hand made impressions.

## Slide 3: Unified Bus Operation (v2.0)
3msb
CE
CE
Data Bus
Data Bus
Data Bus
Instruction Registers
SRAM
EEPROM
Address Bus + Read/Write
Stack Pointer
Program Counter
AMAP
Decoder
MMIO
Micro
Instructions
Read /Write
Register
File
Addr H
Addr L
Base Pointer
TmpAR
16bitAdder
8b16b
AR Select
CE
8 lsb
8 msb
Data Pointer
PC
SP
DP
BP
TmpAR

## Slide 4: ByteFrost Addressing Modes
Immediate
General Register
Address Register
Memory
There are five forms of memory in the ByteFrost – Immediates (read-only), General-Purpose Registers (R0 – R3), Address Registers (DP, SP, PC, BP), Memory (64KB divided into ROM, RAM, and MMIO regions), and Stack
Every solid directed edge (u, v) in the following graph means that memory u can write to memory v with a dedicated instruction.
Every dotted directed edge (u, v) means that the memory u can write to memory v indirectly (i.e., a path exists from u to v but requires multiple instructions to implement).
There are technically 5 x 5 = 25 possible permutations here, but as immediates are read-only, there are in effect only 5 x 4 = 20 possible permutations.
Instructions with an asterisk (*) are currently not implemented.
Src | Dest | Semantics | Dedicated Instruction?
Imm | GR | Rd = Imm_8 (LDR Rd, Imm) | Yes (LDR)
GR | GR | Rd = Rs (MOV Rd, Rs) | Yes (MOV)
AR | GR | Rd = ARSrc[L/H] | Yes (*)
Memory | GR | (LMA) Rd = *{%DP[H], Imm}, DP[L] = Imm (LMR) Rd = *{%DP[H], Rs}, DP[L] = Rs (LMO*) Rd = *(ARSrc + Imm) | Yes (LMA, LMR, *
Stack | GR | Rd = *(SP), SP++ | Yes (POP)
Stack
LDR
MOV
Src | Dest | Semantics | Dedicated Instruction?
Imm | AR | ARDest[L/H] = Imm | Yes (*)
GR | AR | ARDest[L/H] = Rs | Yes (*)
AR | AR | ARDest = ARSrc + Imm | Yes (*)
Memory | AR | ARDest[L/H] = *(ARSrc + Imm) (?) ARDest = *{ARSrc + Imm + 1, ARSrc + Imm} (?) | No
Stack | AR | ARDest = *{SP + 1, SP}, SP += 2 (?) (e.g. POP ARDest) | No
Src | Dest | Semantics | Dedicated Instruction?
Imm | Memory | *(ARSrc) = Imm (?) | No
GR | Memory | *(ARSrc + Imm) = Rs | Yes (*)
AR | Memory | *(ARDest + Imm + 1, ARDest + Imm) = ARSrc(?) | No
Memory | Memory | *(ARDest + Imm) = *(ARSrc) | No (load-store architecture)
Stack | Memory | *(ARSrc + Imm) = *SP, SP++ (?) | No
Src | Dest | Semantics | Dedicated Instruction?
Imm | Stack | *(SP) = Imm, SP– (Push Imm) | No?
GR | Stack | *(SP) = Rs, SP-- | Yes (PUSH *) (change to full-descending)
AR | Stack | *(SP, SP – 1) = ARSrc, SP -= 2 | No? (Push ARSrc)
Memory | Stack | ? | ?
Stack | Stack | ? | ?

## Slide 5: Backplane
sc709_v1.0.0_2023-04-17_22-11_schematic.pdf
EasyEDA(Standard) - A Simple and Powerful Electronic Circuit Design Tool
42
43
44
42
43
44
37
38
39
37
38
39

## Slide 6: Main Backplane
__41 | 41 | 1 | A15
__42 | 42 | 2 | A14
__43 | 43 | 3 | A13
__44 | 44 | 4 | A12
__45 | 45 | 5 | A11
__46 | 46 | 6 | A10
D0 | 47 | 7 | A9
D1 | 48 | 8 | A8
D2 | 49 | 9 | A7
D3 | 50 | 10 | A6
D4 | 51 | 11 | A5
D5 | 52 | 12 | A4
D6 | 53 | 13 | A3
D7 | 54 | 14 | A2
CTRL23 | 55 | 15 | A1
CTRL22 | 56 | 16 | A0
GND | 57 | 17 | GND
+5V | 58 | 18 | +5V
CTRL21 | 59 | 19 | __19
CTRL20 | 60 | 20 | Reset#
CTRL19 | 61 | 21 | CLK
CTRL18 | 62 | 22 | WR#
CTRL17 | 63 | 23 | RD# (OE#)
CTRL16 | 64 | 24 | INSTR0
CTRL15 | 65 | 25 | INSTR1
CTRL14 | 66 | 26 | INSTR2
CTRL13 | 67 | 27 | INSTR3
CTRL12 | 68 | 28 | INSTR4
CTRL11 | 69 | 29 | INSTR5
CTRL10 | 70 | 30 | INSTR6
CTRL9 | 71 | 31 | INSTR7
CTRL8 | 72 | 32 | INSTR8
CTRL7 | 73 | 33 | INSTR9
CTRL6 | 74 | 34 | INSTR10
CTRL5 | 75 | 35 | INSTR11
CTRL4 | 76 | 36 | INSTR12
CTRL3 | 77 | 37 | INSTR13
CTRL2 | 78 | 38 | INSTR14
CTRL1 | 79 | 39 | INSTR15
CTRL0 | 80 | 40 | __40
Orange pins have jumpers that can make them local
Pin with prefix __ are not assigned

## Slide 7: Secondary Backplane
__41 | 41 | 1 | Bus_Request
__42 | 42 | 2 | Bus_Grant
__43 | 43 | 3 | Bus_Release
__44 | 44 | 4 | Quiesce
__45 | 45 | 5 | 
__46 | 46 | 6 | Fetch_Cycle
 | 47 | 7 | 
 | 48 | 8 | Display_Load
 | 49 | 9 | KBD_CLK
 | 50 | 10 | KBD_Data
 | 51 | 11 | 
 | 52 | 12 | 
 | 53 | 13 | 
 | 54 | 14 | 
 | 55 | 15 | 
 | 56 | 16 | 
GND | 57 | 17 | GND
+5V | 58 | 18 | +5V
 | 59 | 19 | BPL_LD
 | 60 | 20 | BPH_LD
 | 61 | 21 | SPL_LD
 | 62 | 22 | SPH_LD
 | 63 | 23 | DPL_LD
 | 64 | 24 | DPH_LD
 | 65 | 25 | PC_LD#
 | 66 | 26 | DHPC_LD
 | 67 | 27 | TmpAR_OE#
 | 68 | 28 | BP_OE#
 | 69 | 29 | SP_OE#
 | 70 | 30 | DP_OE#
 | 71 | 31 | PC_OE#
 | 72 | 32 | __32
LD_BRNCH | 73 | 33 | __33
FLAG_N | 74 | 34 | __34
FLAG_C | 75 | 35 | __35
FLAG_Z | 76 | 36 | __36
RST_MicroPC | 77 | 37 | __37
MSB_Quiesce | 78 | 38 | __38
ARSrc_0 | 79 | 39 | __39
ARSrc_1 | 80 | 40 | __40
Orange pins have jumpers that can make them local
Pin with prefix __ are not assigned

## Slide 8: Area Estimation – Chips * Length
1. clock
2. CTRL LEDs
3. MicroInst
4. OE/WE
5. ROM
6. DP
7. SRAM
8. PC
9 Addr
10. Counter
11. RNG
12. OpCode
13. Regs
15. Branch | 14. Display
16. SD MKR
17. SD I/F
18. BP
19. AddrDisp
20. TmpAR
21. KBD
22. SP
23. Arduino+ Display
24. ALU

## Slide 9: Motherboard (v3.0)
The 4 buttons and LEDs at the bottom preserve the original ByteFrost design
The clock is replaced with a crystal.
The clock control is through the jumpers next to the crystal
The 7SEG displays are scanned, such that one decoder serves 4 digits.
The Display is planned to stand on 45mm columns
16b rainbow need to connect the display to the motherboard
The empty space is to allow easy access to the EEPROM release bar
The Primary and Secondary busses provides 160 lines to the rest of the system

## Slide 10: Motherboard Clock (v3.0)

## Slide 11: Motherboard Address Display (v3.0)

## Slide 12: Motherboard Data and Opcode Display (v3.0)

## Slide 13: Motherboard EEPROM (v3.0)
In v3.0, the Chip_Enable signals are distributed, i.e, each storage need to generate its own CE based on the address bus.
In this case the three MSBs are OR-ed to generate CE# for the lower 8KB

## Slide 14: Motherboard Arduino Interface (v3.0)
DISP_LD – trigger printing a CHAR on the display
First 273 capture the CHAR and second captures the A/I
LDISP_LD also goes to the Arduino to trigger interrupt
The Keyboard CHAR is serialized from Arduino and processed elsewhere through the secondary backplane.
The reset line to Arduino need to be disconnected to enable programming through the USB

## Slide 15: Display Load (V2.0)
Display Load
µC 6: Out Reg H
µC 3: Reg Out Select
OpCode_08
OpCode_0D
Main CLK
273 Char
Data Bus
Disp Char
15
273 A/I
OpCode [5] A/I
A/I

## Slide 16: Debug & Reset (v3.0)
The LM555 one-shots are used as debouncers, i.e. unify the many fast transitions a button may create.
E.g. a “Single Step” button may advance multiple addresses unless a debouncer will unify the transitions into a single press.
The CLK_GATING is a special timer that extend RST to almost 2sec. This allows the Arduino handling the display sufficient time. Otherwise, the first characters that printed in that time will be lost.
74HC76 is the running-state FF which determines if the system is:
  RUN_STATE: RUNNING_CLK becomes CLK
  HALT_STATE: No clock, or S_STEP is the CLK
The BREAK and CONT do not need debouncers as they reset or set running-state
74HC02 is an OR
The State wires are ORed with the clock they mask. (The output of the OR is ‘1’ instead of clock)
74HC00 is a NAND
The two masked clocks are combined with a NAND (the masked clock is 1, enabling the other to go through the NAND)
Another NAND is gated to allow the 2sec for the Display
Next slide from v2.0 might help to visualize this

## Slide 17: Clock Gating (v2.0)
74LS76
Running CLK
Op Code 1: BRK
Reset#
BRK Button
(Purple)
Cont. Button
(Gray)
S.S. CLK
Running CLK
Reset
Main Reset
Main CLK
Reset LED
(Orange wire)
RUN LED
(Brown wire)
Halt LED
(Blue wire)
Clock LED
(Green wire)
Reset Button
(Red wire)
4ms
2s
Clock gating 2sec for
Arduino (display) to boot
17

## Slide 18: Display Daughterboard (v3.0)
The Display daughterboard is a mapper between the ByteFrost, the Arduino and the Display
The wire to the motherboard is a 16-wire rainbow to the Motherboard
J1/J2 are the socket for the Arduino
The socket to the display is directly mapped to the display and physically holds the daughterboard in the air underneath the display.
The Arduino is positioned such that the USB socket is as close as possible to the left edge of the Display, on the far end from the backplane of the Motherboard

## Slide 19: Display (V2.0)
Disp Char
5 4 3 2 1 0
6 7
Display Load
INT0
Notes:
To free up 4 GPIOs, Display is configured to use 4b which requires two writes
5v was added to allow independence of USB connection. When USB is connected, it helps the main supply
To enable programing, the reset line need to be disconnected – proposed to add a 3state on its path
“A/I” is now latched and stay valid for multiple clocks and does not fail at MAX clock
IDE Setup: Board "Arduino NANO“; CPU "ATmega328p (old bootloader)"
USB Serial.Print
5V
19
A/I
KBD clock
KBD data
KBD
White
Gray
# Main Reset
Notes: 1. IDE Setup
a. Board "Arduino NANO"
b. CPU "ATmega328p (old bootloader)"
2. To program the Arduino - the RESET control signal (black) need to be disconnected!!.

## Slide 20: Keyboard
“1”
KBD
Clock - White
Data - Gray
#Ready
KBD #OE
11
13
12
RDY
KBD
Data Bus
8
9
1
2
1
3
Notes:
The format of the character is 1 READY bit followed by 8b char
Once the READY bit reaches the 9th spot (RDY Q0) the Char is ready
Once Ready, the Read to KBD generate #OE and the Char is out
If there is no Char, the #OE does not happen, and the CPU read 0
CPU ignores 0 as it is not an ASCII
The #OE also generates a reset that empty the SR but not the register
The end of the #OE generates a Reg clk (RCL), to load 0 to the register
The clock of the SR is inversed as clock to the Register (RCL) (if not inverted, the register get the previous SR)
The RCL combines both clock and #OE through OR 123
It is important that the clock from the display is 0 when not active so it wont block the OR.
2
13
12

## Slide 21: Clock and Debug

## Slide 22: Clock
220
0.1uF
Or
10uF
100Ω
9.3kΩ
Parts | Min | Frequency
0.01uF (103) | 5KHz | 420KHz
R2=100 |  | 
Rpin5=10K |  | 
2
6
Single Step
(Yellow wire)
S.S. CLK
Running CLK
10KΩ
R on pin 5:
The design of using Vout as power for charging C1 generates 50% duty cycle only if Vout==Vcc. In reality, it is lower and the capacitor takes more time to reach the higher trigger point and duty cycle without it is only 33%.
With 10K on pin 5, both triggering points become lower, closer to 1/3 and 2/3 of Vout (instead of Vcc). That provides 50% duty cicle,also increase the frequency because the distance between the points is smaller (increasing the max frequency of this design from 250hHz to 420kHz)
22

## Slide 23: Reset

## Slide 24: Registers File

## Slide 25: Register Out Select

## Slide 26: Address Bus Select (ARSelect) v2.0
ARSelect 8x8 LUT
Inputs |  |  |  |  |  |  | Outputs (Active Low)
Bus Grant (A7) | Fetch Cycle (A6) | PC Out control signal (A5) | SP Out control signal (A4) | TmpAR Write control signal (A3) | Opcode_MAG_LDW_SDW_MAA (Active Low) (A2) | AR Src operand (A1, A0) | 
1 | X | X | X | X | X | X | None (Bus floats)
0 | 1 | X | X | X | X | X | PC (I/O 0)
0 | 0 | 1 | X | X | X | X | PC (I/O 0)
0 | 0 | 0 | 1 | X | X | X | SP (I/O 2)
0 | 0 | 0 | 0 | 1 | X | X | TmpAR (I/O 4)
0 | 0 | 0 | 0 | 0 | MAG, LDW, SDW, MAA | AR Src[1:0] | = AR Src[1:0] 0-PC, 1-DP, 2-SP, 3-BP
0 | 0 | 0 | 0 | 0 | Other Opcodes | X | DP (I/O 0)
ARSelect specifies which AR gets to write to the Address Bus and whether any of them do (it can do this since it only sends output enables; if it doesn’t send an output enable to any hardware entity, then no entity writes to the address bus).
EEPROM Data Output Bit | Output
7 | 1 (unused)
6 | 1 (unused)
5 | 1 (unused)
4 | TmpAR Output Enable (ACTIVE LOW)
3 | BP Output Enable (ACTIVE LOW)
2 | SP Output Enable (ACTIVE LOW)
1 | DP Output Enable (ACTIVE LOW)
0 | PC Output Enable (ACTIVE LOW)
Bus Grant
FetchCycle
Program Counter OE
µC 9: PC Out
µC 14: SP Out
Stack Pointer OE
µC 20: TmpARWrite
Opcode_MAG_LDW_SDW_MAA
ARSrc [1:0]
Data Pointer OE
TmpAR OE
Base Pointer OE

## Slide 27: Opcode_MAG_LDW_SDW_MAA (v2.0)
74LS30
LDWL
OpCode_14
LDWH
OpCode_15
SDWL
OpCode_16
SDWH
OpCode_17
MAAL
OpCode_18
MAAH
OpCode_19
MAG
OpCode_1A
Opcode_MAA
OpCode_10
JSR
Opcode_MAA_JSR
Opcode_MAG_LDW_SDW_MAA

## Slide 28: ARSrc Operand Decode v2.0
ARSrc [1:0]
157: ARSrc
Instr[5],Instr[1]
ARSrc Decode:
If opcode is of (AR  GR) (Rd = ARSrc[L/H]) instruction, then ARSrc is in bits 9:8.
Otherwise, ARSrc is a function of bits 5 and the opcode (maybe the opcode’ least significant bit?)
Instructions that specify ARSrc with 1 bit in bit 5 need to get the other bit from the opcode; if we always assign these two-opcode instructions opcodes as [4-bit opcode x][0/1], then we can get the other ARSrc bit from the least significant bit of the opcode, i.e., in these instructions ARSrc is {Instr[5], Instr[0]} (in bits 5 and 0)
Instr[9],Instr[8]
Instr[9],Instr[8]
Instr[5],Instr[1]
0v
OpCode_MAG

## Slide 29: Address Map Decoder (v2.0)
0000 – 1FFF | ROM
2000 – 3FFF | RAM
4000 – 5FFF | 
6000 – 7FFF | 
8000 – 9FFF | 
A000 – BFFF | 
C000 – DFFF | 
E000 – FFFF | MMIO
138 AMAP
138 AMAP
~SRAM Chip En
74HC21
74HC21
~EEPROM Chip En
Address Bus + Read/Write
A15..A13
138 MMIO Device Enable
A12
A11
A10
A9
~SD Card Device En
MMIO
E000 – E1FF | SD Card
E200 – E3FF | Counter
E400 – E5FF | 
E600 – E7FF | 
E800 – E9FF | 
EA00 – EBFF | 
EC00 – EDFF | 
EE00 – EFFF | 
F000 – FFFF | No HW
Address Map
~Counter Device En

## Slide 30: Memory Access (v2.0)
Cycle | Signal | SRAM | EEPROM | MMIO
Memory Write | #WE | #WE | ‘1’ (no writes) | #WE
Memory Read | #OE | #OE |  | 
Memory Write, or Memory Read | #CE | (~SRAM Chip En) | (~EEPROM Chip En) | MMIO
µC 10: MEM Read
FetchCycle
#OE
Main CLK
µC 11: MEM Write
#WE
Bus Grant
4
5
6
148ns delay
OR+Delay postpones the start of #OE,
but doesn’t impact its end

## Slide 31: SRAM (v2.0)
Data
Bus
I/O[0:7]
SRAM
A0..A15
31
Address Bus + Read/Write
~SRAM Chip En
#OE
#WE

## Slide 32: EEPROM (v2.0)
Data Bus
Prog EEPROM
Addr
[15:0]
Prog
Data[7:0]
32
Address Bus
~EEPROM Chip En
#OE

## Slide 33: Address Registers - Data Bus Load Enable v2.0
AR DB LE 8x8 LUT
EEPROM Address Bit | Input
7 | PC Ld Branch (Flags & µC 8: PC Load)
6 | loadAR (control signal)
5 | PC Load (control signal)
4 | loadARHorL (control signal)
3 | Opcode_MAA (ACTIVE LOW)
2 | (AR) L/H instruction operand
1 | ARDest[1]
0 | ARDest[0]
EEPROM Data Output Bit | Output
7 | BP[H] Load Enable (574 - ACTIVE HIGH)
6 | BP[L] Load Enable (574 - ACTIVE HIGH)
5 | SP[H] Load Enable (191 – ACTIVE High*)
4 | SP[L] Load Enable (191 - ACTIVE High*)
3 | DP[H] Load Enable (574 - ACTIVE HIGH)
2 | DP[L] Load Enable (574 - ACTIVE HIGH)
1 | DHPC Load Enable (574 - ACTIVE HIGH)
0 | PC[L] Load Enable (161 - ACTIVE LOW)
µC 8: PC Load
PC Ld Branch
PC Ld En
µC 18: LoadAR H/L
µC 17: LoadAR
Opcode_MAA
Opcode_5
Opcode_7
Opcode_6
DHPC Ld En
DP[L] Ld En
DP[H] Ld En
SP[L] Ld En
SP[H] Ld En
BP[L] Ld En
BP[H] Ld En
Main CLK
* 191 is active low, but to use the AND for clock gating they are Active High that later inverted

## Slide 34: Program Counter Design
The Program Counter on Address Bus is a 16b pointer, with granularity of bytes.
However, the actual HW counter is a 15b counter, counting instructions.
So:
  When SW writes to the HW counter, the data shift right, dropping the lsb (PC cannot be odd)
  When HW Counter writes to the Address bus, it shift left, addith the lsb from the fetch FSM
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Load PC from Data+Dummy
HW Program Counter
PC on the Address Bus
Load PC from Dummy
Load PC from Data Bus
dangled
Bit[0] from
Fetch FSM
0
dangled

## Slide 35: Program Counter (v2.0)
74HC245
74HC161 PC[15:13]
74HC161 PC[12:9]
74HC161 PC[8:5]
74HC161 PC[4:1]
PC Low[8:1]
~Main Reset
Main CLK
INC Prog Counter
74HC245
35
Data
[4:1]
Data
[7:5]
Address Bus
Addr Low
[8:1]
Addr Hi
[15:9, 0]
Program Counter OE
PC[7:0 ] Addr[8:1]
PC[14:8]  Addr[15:9]
INC  Addr[0]
574: Prog Ctr
Dummy
Data Bus
DHPC Ld En
PC Ld En
0,[15:9]
[0]
PC High[15:9]
Notes:
In SW view, PC points to Address,
In HW view, PC points to instruction (div by 2)
Read PC : PC shifts left
  “INC Prog Counter” provides bit 0
Write PC: (Absolute Branch, JSR, RTS) Dummy and Data shifted right (ignoee lsb)
‘0’
PC
[4:1]
PC
[8:5]
PC[8]
Data[0] dangled

## Slide 36: Data Pointer (v2.0)
!Clk
Control
AND
Clk
36
Address Bus + Read/Write
574: Addr Ptr Lo
A7..A0
A15..A8
574: Addr Ptr Hi
Data Pointer OE
Data
Bus
A7..A0
A15..A8
DP[L] Ld En
DP[H] Ld En
Data is sampled in the middle of the clock (negative edge)

## Slide 37: Base Pointer (v2.0)
!Clk
Control
AND
Clk
37
Address Bus + Read/Write
574: Addr Ptr Lo
A7..A0
A15..A8
574: Addr Ptr Hi
Data
Bus
A7..A0
A15..A8
BP[L] Ld En
BP[H] Ld En
Base Pointer OE
Data is sampled in the middle of the clock (negative edge)

## Slide 38: Stack Pointer (v2.0)
Data
Bus
574: Stack Ptr Page
µC 15: SP Count
µC 16: SP Up/Down
38
Address Bus + Read/Write
A7..A0
A15..A8
A7..A4
Stack Pointer OE
A3..A0
SP[H] Ld En
SP[L] Ld En
SP 7:4
SP 3:0
Main CLK
74HC191
A3:A0
74HC191
A7:A4
74HC191
A11:A8
74HC191
A15:A12
574: Stack Ptr Page
A15..A12
A11..A8
SP 7:4
SP 3:0

## Slide 39: Address to Data Bus
574: Addr Hi
574: Addr Lo
Address Bus
Data
[7:0]
Data
[7:0]
Main CLK
Addr Hi
[15:8]
Addr Hi
[15:8]
Data Bus
CD4053 A
0
1
CD4053 B
0
1
CD4053 C
0
1
µC 22: AB2DB H/L
µC 21: AB2DB
1
1
Opcode_MAA_JSR
AR H/L (Instr[5])
0v
0v
0v
5v
Opcode_MAA_JSR
µC 22: AB2DB H/L
AR H/L (Instr[5])
1v
1v
Addr Hi OE
Addr Lo OE
µC 21: AB2DB
µC 21: AB2DB
Addr Hi OE
Addr Lo OE
11
13
12
8
10
9
11
9
10
12
13
14
3
5
4
1
2
15
Bock clock during Output Enable

## Slide 40: TmpAR (Address Offset Adder) v2.0
Addr Lo
[7:0]
TmpAR OE
574: TmpAR Hi
574: TmpAR Lo
Address Bus
Addr Low
[7:0]
Addr Hi
[15:8]
Main CLK
283: Add 3:0
283: Add 3:0
283: Add 3:0
283: Add 3:0
Addr Hi
[15:8]
Addr Hi
[15:8]
Address Bus
Data Bus
Addr Hi
[15:8]
Data
Sign Extended
[15:8]
Data
[7:0]
3
µC 19: TmpARRead
Read in the middle of the cycle
1
2
6
5

## Slide 41: Output H Register to Data Bus (v2.0)
HC245
H  Bus
HC245
H4  Bus
Data
Bus
If opcode is 00110 or 10011, then 4-bit immediate from high instruction register
is written to the bus; otherwise, the full 8-bit high instruction register is written to
bus as an 8-bit immediate
OpCode_13
µC 6: Out Reg H
H Reg
8 bits
41
0
OpCode_6
Short H
[15:12]
ALU Imm
TST Imm

## Slide 42: Fetch State Machine (v2.0)
273 Hi
MR
175
273 Lo
# Reset_microPC
# Main Reset
µC 7: PC Advance
Main CLK
Prog
Data[7:0]
Prog
Data[7:0]
OpCode
[4:0]
H Reg
8 bits
OpCode
[7:5] Flags
OpCode
[7:6] Rd RO
Short H
[15:12]
OpCode
[7:6] Rd RI
OpCode [5] A/I
42
INC Prog Counter
Quiesce
FetchCycle
Bus Grant
MSB_Quiesce
# Bus Grant

## Slide 43: Micro Instructions EEPROMs (v2.0)
Counter A2..A0
Micro Ins 8_15
1,0,0,0,0,0,0,0
1,0,0,0,0,0,0,0
µC 7: PC Advance
µC 6: Out Reg H
µC 5. Reg In En
µC 4: Reg Out En
µC 3: Reg Out Select
µC 2: ALU Out En
µC 1: ALU Load A
µC 0: ALU Load B
µC 5. Reg In En
µC 4. Reg Out En
Micro Ins 0_7
5 bit
0,0
0,0
3 bit
3 bit
5 bit
Opcode A7..A3
µC 2. ALU Out En
µC 15: SP Count
µC 14: SP Out
µC 13: Reg Out Rd
µC 12: Ld Data Addr
µC 11: MEM Write
µC 10: MEM Read
µC 9: PC Out
µC 8: PC Load
161
3 bit
Main CLK
# Reset_microPC
OpCode
[4:0]
Micro Ins 16_23
1,0,0,0,0,0,0,0
5 bit
0,0
3 bit
µC 23:
µC 22: AB2DB H/L
µC 21: AB2DB
µC 20: TmpARWrite
µC 19: TmpARRead
µC 18: LoadAR H/L
µC 17: LoadAR
µC 16: SP Up/Down
43
Set A8 to quiesce all controls during the first clock while upper OpCode is loading
MSB_Quiesce

## Slide 44: Sharing the Data and Address Buses during Fetch Cycle
Data Bus
Address Bus
Last Micro instruction
PC Advance
Addr+1
Inst address A8=1
Program Counter
Low addr
Program Counter
High addr
Ld Low Instruction
Last Instruction
Next Instruction
Control signals
Clock
Next Instruction Low byte
Next Instruction High byte
Ld High Instruction
Ld Instruction
Last clock of an instruction includes the PC_Advance.
In that clock, the Address and Data buses are used by the Program Counter. No other signal using the address or data buses is allowed.
First clock of the next instruction, buses are used to load the high byte of the instruction. To avoid transmission of the first micro instruction on the buses, the micro instruction address bit A8 is set, and all control signals are set to 0, avoiding any transmission on the busses
Micro Instruction 0 controls the buses
Micro
instruction 0
Micro
instruction 1

## Slide 45: PC Advance - Logic Analyzer
PC Advance
Address Bus controlled by Prog Count
Ld Low (rising)
INC, Quiesce
Ld High
(from INC)
Reset Micro Instruction Ctr
CTR=0
CTR=0
CTR=1
CTR=2

## Slide 46: Bus Arbitration for I/O
Normal
CPU owns buses
MMIO Buses Request
No change
CPU owns buses till end of instruction
MMIO Buses Granted
CPU does not transmit on
  Address bus
  Data bus
  Micro instruction controls
Microinstruction counter held in reset
Bus Request
MMIO request
End of
Micro instruction
Bus Release
# Bus Release
Bus Grant
Quiesce
Requested
175
4
5
6
1
2
3
5
4
6
1
2
3
12
13
11

## Slide 47: SD Card – Page Load / Store
6
7
8
9
10
11
12
13
14
RESET
GND
VCC (3.3v)
VIN (5v)
5V
574 Addr - High
3.3v – 5v
bi-directional
level shifters
8-bit data bus
Addr 15:8
9 - CNT/CLK
10 – RESET Counters
Address | R/W | Register
Base Addr | W | Addr Hi
+1 | W | Sector Hi
+2 | W | Sector Lo
+3 | W | Go
8 - GO_INT
11 - Serial_IN
12 - Shift
17 – ReadRAM#
16 – WriteRAM#
3:0 Ctr
7:4 Ctr
Addr 7:4
Addr 3:0
165 Sector Hi
165 Sector Lo
165 Sector Hi
Data bus
138 Decoder
Load Addr Hi
Ld Sector
Addr 2:0
Data bus
Operation | ReadRAM# | WriteRAM# | Addr_En# | Dat_ dir | SRAM OE# | SRAM WE#
Idle | 0 | 0 | 1 | N/A | N/A | N/A
RAM  SD | 0 | 1 | 0 | In | 0 | 1
SD  RAM | 1 | 0 | 0 | Out | 1 | 0
Idle | 1 | 1 | 1 | N/A | N/A | N/A
Addr_en#
Addr_en#
WriteRAM#
HC245 Data Out
HC245 Addr Out
~SD Card Device En
Addr_en#
47
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Addr_en#
XNOR
#WE
Bus Grant
Bus Request
# Main Reset
# Bus Release

## Slide 48: Counter (v2.0)
Addr 2:0
Read Decoder
Write Decoder
#OE
#WE
~Counter Device En
Addr 2:0
Data Bus
74HC590 Counter
74HC590 Counter
74HC590 Counter
74HC590 Counter
74HC590 Counter
MRC: Reset Counter
CPR: Latch Counter
Address | R/W | Register
Base Addr E200 | W | Reset Counter
+1 | W | Latch Counter
+2 | R | Read Counter 0
+3 | R | Read Counter 1
+4 | R | Read Counter 2
+5 | R | Read Counter 3
+6 | R | RNG Read
RNG Rd

## Slide 49: RNG (V2.0)
RNG Rd
Data Bus
HC164
1
2
3
4
5
6
10
11
8
9
1
2
3
4
5
6
9
10
8
13
12
11
Clock
5v

## Slide 50: OpCode Decoder (v2.0)
74HC138
OpCodes 24-31
0
1
2
74HC138
OpCodes 8-15
74HC138
OpCodes 0-7
74HC138
OpCodes 16-23
OpCode
[4:0]
0
1
2
3
4
OpCode_6
OpCode_08
OpCode_0D
OpCode_7
‘0’
‘0’
‘1’
50
OpCode_05
OpCode_10
OpCode_11
Branch Absolute
JSR
RTS
Branch Relative
OpCode_1
BRK
ALU Immediate
Out Reg
Out Imm
0
1
2
0
1
2
0
1
2
‘0’
‘0’
OpCode_18
OpCode_19
OpCode_MAG
OpCode_1B
OpCode_1C
OpCode_1D
OpCode_1E
OpCode_1F
MAAL
MAAH
1A
LDA
MGA
Unused
Unused
Unused
OpCode_13
TST Im

## Slide 51
ALU Interface – Flags, A,B Registers, Op Code selection (v2.0)
ALU
ALU OpCode
Flags
Carry In
74HC251
74HC161
Flags captured on ALU Out (161 Parallel Load Enable)
74HC157
4b’0110 (ADD)
Function H[3:0]
OpCode_7
Gray
0
1
Don’t update flags on BR relative
MR
Clock
Clk
Clk
A_I
µC 2. ALU Out En
µC 1: ALU Load A
µC 0: ALU Load B
74HC161
74HC161
Data
Bus
Data Bus
74HC161
74HC161
A
B
C
Flags
Notes: Registers A and B are implemented by two HC161s, each stores 4 bits as the typical HC273 and HC347 won't fit into the 16pin sockets on the ALU wirewrap board.
The branch relative instruction (Obsolete) doesn’t update flag bits to avoid corrupting the flag register state when executing a branch instruction (which may occur due to the ADD operation performed)
Branch Relative

## Slide 52: ALU OpCodes 2,3,7
ALU opcode(010), SF(0 / 1) – A XOR B / !B
No change to the source SF for ADD/SUB/ADC/SBC/!B
x8
SF
SF
ADD/SUB/ADC/SBC/!B
B or !B
A
8
8
B
Op Code ‘010’ output
Adder
A
Carry-in to Adder
Op Codes
‘011’ , ‘111’
{Op =XX0, SF = 0}  A XOR B; Else B or !B
ALU_Op[0]
0
1
x8
52
Op Select | Special Func. = 0 |  | Special Func. = 1 |  | Flag in
010 - 2 | A XOR B | XOR: 4 | !B | NOT: 5 | -
011 - 3 | A + B | ADD: 6 | A – B | SUB: 7 | -
111- 7 | A + B + Cin | ADC: E | A – B + Cin | SBC: F | Cin
!B or (A XOR B)

## Slide 53: Branch (v2.0)
74HC151
Flags
74HC161
‘1’
‘N’
‘C’
‘Z’
D4
D5
D6
D7
Q7 Q6 Q5
Instruction LSB
C2 | C1 | C0 | Condition | Instruction LSB | Equivalent Assembly Instruction
0 | 0 | 0 | JMP | 05 | JMP
0 | 0 | 1 | N | 25 | BMI – Branch on Minus
0 | 1 | 0 | C | 45 | BCS – Branch Carry Set
0 | 1 | 1 | Z | 65 | BEQ – Branch Equal
1 | 0 | 0 | Never | 85 | NOP
1 | 0 | 1 | !N | A5 | BPL – Branch on Plus
1 | 1 | 0 | !C | C5 | BCC – Branch Carry Clear
1 | 1 | 1 | !Z | E5 | BNE
µC 8: PC Load
OpCode
[7:5]
PC Ld Branch
Note: PC Ld Lo is renamed to PC Load Branch.

## Slide 54: Instruction set (v2.0)
Op code | Instruction | Details
0x00 | NOP | No operation
0x01 | BRK | Halt the program
0x02 | ALU (Format ALU Rd, Rs1, Rs2) | ALU instruction (OR, AND, XOR, NOT, ADD, SUB, ASL, ROL, LSR, ASR, ROR, ADC, SBC)
0x03 | LDR | Load Register from immediate
0x04 | MOV | Copy Register (MOV instruction in ARM)
0x05 | Branch Absolute | Conditional/Unconditional Jump to a 16-bit address
0x06 | ALU Immediate (Format: ALU Rd, Rd, imm) | ALU instruction with value from immediate
0x07 |  | 
0x08 | OUT register | Print a register as a character or integer
0x09 |  | 
0x0A |  | 
0x0B |  | 
0x0C |  | 
0x0D | OUT Immediate | Print the immediate next byte as a character or integer
0x0E | PUSH | 
0x0F | POP | 
0x10 | JSR | Jump Subroutine, store current PC in stack
0x11 | RTS | Return Subroutine, Load PC from stack
0x12 | TST Registers | Compare registers
0x13 | TST Register | Compare register and immediate
0x14 | LDW1 | Load Data Byte with Offset 1 (PC or SP)
0x15 | LDW2 | Load Data Byte with Offset 2 (DP or BP)
0x16 | SDW1 | Store Data Byte with Offset 1 (PC or SP)
0x17 | SDW2 | Store Data Byte with Offset 2 (DP or BP)
0x18 | MAA1 | Move Address with Offset to Address 1 (PC or SP)
0x19 | MAA2 | Move Address with Offset to Address 2 (DP or BP)
0x1A | MAG | Move Address to General register
0x1B | LDA | Load Address register
0x1C | MGA | Move General to Address register
Covered by BIST
Implemented
Planned
Deprecating
Not used
54

## Slide 55: ALU with changes
Op Select | Special Func. = 0 |  | Special Func. = 1 |  | Flag in | Flags Out
0 | A OR B | OR: 0 | A OR B |  | - | Z, N
1 | A AND B | AND: 2 | A AND B |  | - | 
2 | A XOR B | XOR: 4 | ~B | NOT: 5 | - | Z, N
3 | A + B | ADD: 6 | A – B | SUB: 7 | - | Z, N, Co
4 | Shift Left A A[0]=0 | ASL: 8 | Rotate left A A[0]=Cin | ROL: 9 | Cin (Rotate) | Z, N=A[6], Co=A[7]
5 | Shift Right A | LSR: A | Arithmetic S.R. A | ASR: B | - | Z, N, Co=A[0]
6 | Rotate Right | ROR: C | Cin -> A-> Cout |  | Cin | Z, N, Co=A[0]
7 | A + B + Cin | ADC: E | A – B + Cin | SBC: F | Cin | Z, N, Co
Proposals for the additional operations
How to chain Shift Right of two bytes?
Proposal | # of IC slots | Description | Op Code
OR and ADD share Op Code (low priority) | 2x 74LS157 | Special Function select OR or AND | Release op code
Allow using ALU as two registers (low Priority) |  | Need to create output A and B | 
55

## Slide 56: Micro-Instructions Control: NOP Instruction (00000)
Cycle # | Instruction | Explanation
0 | 10000000 = 0x80 | Increment PC
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
0
NOP
56
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
None | XX | X | XXXX | XX | X | OpCode=00

## Slide 57: Micro-Instructions Control: BREAK (00001)
Cycle # | Instruction | Explanation
0 | 10000000 = 0x80 | Increment PC
1 |  | 
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
1
BRK
57
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Note: BRK has the same microcode as NOP, but the opcode decoder halts the clock when the opcode 00001 is detected. Stepping through it manually (via Single-Step / Run button press) resumes the clock. Hence, BRK acts as a hardware breakpoint.
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
None | XX | X | XXXX | XX | X | OpCode=01

## Slide 58: Micro-Instructions Control: ALU (00010)
Cycle # | Instruction | Explanation
0 | 00010010 = 0x12 | Load Rs1 to reg A
1 | 00011001 = 0x19 | Load Rs2 to reg B
2 | 00100100 = 0x24 | Output and Read to Rd
3 | 10000000 = 0x80 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
ALU | Rs2 | Rs1 | S2 S1 S0 SF (Function sel) | Rd | X | OpCode=02
2
ADD Rd, Rs1, Rs2
58
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 59: Micro-Instructions Control: Load Immediate to Reg (00011)
Cycle # | Instruction | Explanation
0 | 01100000 = 0x60 | Write imm to bus and Rd read
1 | 10000000 = 0x80 | Increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Imm | Immediate (8-bit) |  | Immediate (8-bit) | Rd | X | OpCode=03
3
LDR Rd, #0x00
59
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 60: Micro-Instructions Control: MOV (00100)
Cycle # | Instruction | Explanation
0 | 00110000 = 0x30 | Write Rs1 to bus and Rd reads
1 | 10000000 = 0x80 | Increment PC
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Load Reg | XX | Rs1 | XXXX | Rd | X | OpCode=04
4
MOV Rd, Rs1
60
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 61: Micro-Instructions Control: Branch / Jump Absolute Immediate (00101)
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 5 | 4 3 2 1 0
Branch | Immediate (8-bit) |  | Immediate (8-bit) | C2 C1 C0 | OpCode=05
Cycle # | Instruction | Explanation
0 | 0x1_40 01_0100_0000 | Write H register to bus and PC (conditionally) reads
1 | 0x0_80 00_1000_0000 | PC advance
2 |  | 
3 |  | 
4 |  | 
5 |  | 
6 |  | 
7 |  | 
C2 | C1 | C0 | Condition | Low instruction register | Assembly
0 | 0 | 0 | JMP | 05 | JMP
0 | 0 | 1 | N | 25 | BMI – Branch on Minus
0 | 1 | 0 | C | 45 | BCS – Branch Carry Set
0 | 1 | 1 | Z | 65 | BEQ – Branch Equal
1 | 0 | 0 | Never | 85 | NOP
1 | 0 | 1 | !N | A5 | BPL – Branch on Plus
1 | 1 | 0 | !C | C5 | BCC – Branch Carry Clear
1 | 1 | 1 | !Z | E5 | BNE
5
61
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 62: Micro-Instructions Control: ALU immediate (4-bit) (00110)
Cycle # | Instruction | Explanation
0 | 10_0000_0001_0010 = 2012 | Load Rd to reg A
1 | 0100_0001 = 0x0041 | Load 4 bit imm to reg B
2 | 0010_0100 = 0x0024 | Write ALU output to Rd
3 | 1000_0000 = 0x0080 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
Type | 15 14 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
ALU | 4-bit imm. | S2 S1 S0 SF (Function sel) | Rd | X | OpCode=06
6
ADD Rd, #0x00
62
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 63: Micro-Instructions Control: Branch / Jump Relative Immediate (00111)
Cycle # | Instruction | Explanation
0 | 10_0000_0010 0x2_02 | Load PC into reg A
1 | 00_0100_0001 0x0_41 | Load immediate into reg B
2 | 01_0000_0100 0x1_04 | Output ALU val, load PC
3 | 00_1000_0000 0x0_80 | Advance PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
C2 | C1 | C0 | Condition | OpCode | Assembly
0 | 0 | 0 | JMP | 07 | JMP
0 | 0 | 1 | N | 27 | BMI – Branch on Minus
0 | 1 | 0 | C | 47 | BCS – Branch Carry Set
0 | 1 | 1 | Z | 67 | BEQ – Branch Equal
1 | 0 | 0 | Never | 87 | NOP
1 | 0 | 1 | !N | A7 | BPL – Branch on Plus
1 | 1 | 0 | !C | C7 | BCC – Branch Carry Clear
1 | 1 | 1 | !Z | E7 | BNE
7
63
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 5 | 4 3 2 1 0
Branch | Immediate (8-bit) |  | Immediate (8-bit) | C2 C1 C0 | OpCode=07
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Note: This only sets the PC Low register! As such, this instruction is Deprecated.

## Slide 64: Micro-Instructions Control: OUT (01000) (Display ASCII or Integer)
Cycle # | Instruction | Explanation
0 | 0000_0000 = 0x00 | Wait for H register to be loaded (need value of Rs1)- No longer required
1 | 0001_0000 = 0x10 | Write Rs1 to the bus (when opcode 01000 is detected, the value on the bus is read by the OUT register to the display)
2 | 1000_0000 = 0x80 | Advance PC
3 |  | 
4 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Reg | OpCode | XX | Rd | XXXX | Rs1 | XX
8
OUT Rs1, A
64
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Out | XX | Rs1 | XXXX | XX | I=1; A=0 | OpCode=08
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 65: Micro-Instructions Control: OUT immediate (01101)
Cycle # | Instruction | Explanation
0 | 0000_0000 = 0x00 | Wait for H instruction register to be loaded
1 | 0100_0000 = 0x40 | Write program register H to the bus
2 | 1000_0000 = 0x80 | Advance PC
3 |  | 
4 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
Load Reg | OpCode | XX | Rd | XXXX | Rs1 | XX
D
OUT #Imm, A
65
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
Out | 8-bit immediate |  | XXXX | XX | I=1; A=0 | OpCode=0D
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 66: Micro-Instructions Control: PUSH (01110)
Cycle # | Instruction | Explanation
0 | 0x00_80_00 | (SP--;) Decrement SP.
1 | 0x00_48_10 | (*SP = Rs1;) Write Rs1 to the Data Bus, Write SP to the Address Bus, and Set Memory to read from the Data Bus.
2 | 0x00_00_80 | Advance PC.
66
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
PUSH | XX | Rs1 | XXXX | XX | X | OpCode=0x0e
E
PUSH R2
SP--;
*SP = Rs1
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 67: Micro-Instructions Control: POP (01111)
Cycle # | Instruction | Explanation
0 | 0x01_c4_20 | (Rd = *SP; SP++;) Write SP to the Address Bus, Set Memory to write to the Data Bus, Set Rd to read from the Data Bus, and increment SP.
1 | 0x00_00_80 | Advance PC.
67
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
POP | XX | XX | XXXX | Rd | X | OpCode=0x0f
F
POP R1
Rd = *SP;
SP++
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 68: Micro-Instructions Control: JSR (10000)
Cycle # | Instruction | Explanation
0 | 0x00_82_00 | (SP--; Address Bus Register High = PC[H];) Write PC to the Address Bus (captured by A2D).
1 | 0x60_48_00 | (*SP = PC[H]) Write SP to the Address Bus, Write A2D High to the Data Bus (PC[H]), Set Memory to store in *SP.
2 | 0x00_82_00 | (SP--; Address Bus Register Low = PC[L]) Write PC to the Address Bus (captured by A2D).
3 | 0x20_48_00 | (*SP = PC[L]) Write SP to the Address Bus, write Address Bus Register Low to the Data Bus (PC[L]), and set Memory to read from the Data Bus.
4 | 0x00_00_00 | (Address Bus Register High = DP[H]) Write DP to the Address Bus.
5 | 0x66_01_00 | (DHPC = DP[H]; Address Bus Register Low = DP[L]) Write DP to the Address Bus, write Address Bus Register High to the Data Bus (DP[H], and set DHPC to load from the Data Bus.
6 | 0x22_01_00 | (PC[L] = DP[L] (and PC[H] = DHPC)) Write Address Bus Register Low to the Data Bus (DP[L]) and set PC[L] to load from the Data Bus.
7 | 0x00_00_80 | Advance PC.
68
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
JSR | XX | XX | XXXX | XX | X | OpCode=0x10
10
JSR
SP--; *SP = PC[H]; SP--;
*SP = PC[L]; PC = DP;
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 69: Micro-Instructions Control: RTS (10001)
Cycle # | Instruction | Explanation
0 | 0x01_80_00 | (SP++;) Increment SP. (Point to Return address HIGH)
1 | 0x06_45_00 | (DHPC = *SP) Write SP to the Address Bus, Set Memory to write to the Data Bus, Set DHPC to read from the Data Bus, and decrement SP.
2 | 0x00_80_00 | SP-- (Point to Return address LOW)
3 | 0x03_45_00 | (PC[L] = *SP) Write SP to the Address Bus, Set Memory to write to the Data Bus, Set PC[L] to read from the Data Bus (and PC[H] = DHPC).
4 | 0x01_80_00 | (SP++;) Increment SP. (POP first half)
5 | 0x01_80_80 | (SP++;) POP second half and Advance PC.
69
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
POP | XX | XX | XXXX | Rd | X | OpCode=0x0f
11
RTS
SP++; DHPC = *SP; SP--;
PC[L] = *SP, PC[H] = DHPC;
SP++; SP++;

## Slide 70: Micro-Instructions Control: Test (10010)
Cycle # | Instruction | Explanation
0 | 0001_0010 = 0x12 | Load Rs1 to reg A
1 | 0001_1001 = 0x19 | Load Rs2 to reg B
2 | 0000_0100 = 0x04 | Output ALU value on bus (but don’t save in register)
3 | 1000_0000 = 0x80 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
ALU | Rs2 | Rs1 | S2 S1 S0 SF (Function sel) | XX | X | OpCode=12
TST Rs1, Rs2
12
70
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 71: Micro-Instructions Control: Test immediate (10011)
Cycle # | Instruction | Explanation
0 | 10_0000_0001_0010 = 0x2012 | Load Rd to reg A
1 | 0100_0001 = 0x0041 | Load 4 bit imm to reg B
2 | 0000_0100 = 0x0004 | Write ALU output to bus (but not to register)
3 | 1000_0000 = 0x80 | Increment PC
4 |  | 
5 |  | 
6 |  | 
7 |  | 
Type | 15 14 13 12 | 11 10 | 9 8 | 7 6 5 4 | 3 2 | 1 0
ALU | OpCode | XX | Rd | Function | Rs1 | Rs2
Type | 15 14 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
ALU | 4-bit imm. | S2 S1 S0 SF (Function sel) | Rd | X | OpCode=13
TST Rd, #0x00
13
71
Bit | Operation
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B
Bit | Operation
17 | Load Special Register
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | RAM Address Select (0: Address register / 1: Stack pointer)
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 72: Micro-Instructions Control: Load Data Byte with Offset 1 (LDW1) (10100)
Cycle # | Instruction | Explanation
0 | 0x08_00_40 | Write Imm to the Data Bus, ARSrc to the Address Bus, and set TmpAR to read from the 16-bit adder.
1 | 0x10_04_20 | Write TmpAR to the Address Bus, Write Memory data word to the Data Bus, and set Rd to read from the Data Bus.
2 | 0x00_00_80 | Advance PC.
72
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
LDW | Immediate (8-bit) |  | Immediate (8-bit) | Rd | ARSrc[1] | OpCode=14 (and ARSrc[0] = 0)
14
INSTR[5] | INSTR[0] | ARSrc Address Register | Command Parameter
0 | 0 | PC ({PC[H], PC[L]}) | %PC
1 | 0 | SP | %SP
LDW R0, %SP, #4
Rd = *(ARSrc + Imm)
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 73: Micro-Instructions Control: Load Data Byte with Offset 2 (LDW2) (10101)
Cycle # | Instruction | Explanation
0 | 0x08_00_40 | Write Imm to the Data Bus, ARSrc to the Address Bus, and set TmpAR to read from the 16-bit adder.
1 | 0x10_04_20 | Write TmpAR to the Address Bus, Write Memory data word to the Data Bus, and set Rd to read from the Data Bus.
2 | 0x00_00_80 | Advance PC.
73
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
LDW | Immediate (8-bit) |  | Immediate (8-bit) | Rd | ARSrc[1] | OpCode=15 (and ARSrc[0] = 1)
15
INSTR[5] | INSTR[0] | ARSrc Address Register | Command Parameter
0 | 1 | DP | %DP
1 | 1 | BP | %BP
LDW R0, %DP, #4
Rd = *(ARSrc + Imm)
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 74: Micro-Instructions Control: Store Data Byte with Offset 1 (SDW1) (10110)
Cycle # | Instruction | Explanation
0 | 0x08_00_40 | Write Imm to the Data Bus, write ARSrc to the Address Bus, and set TmpAR to read.
1 | 0x10_28_10 | Write TmpAR to the Address Bus, write Rs (Rd) to the Data Bus, and set Memory to read from the Data Bus.
2 | 0x00_00_80 | Advance PC.
74
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
SDW | Immediate (8-bit) |  | Immediate (8-bit) | Rs (Rd) | ARSrc[1] | OpCode=16 (and ARSrc[0] = 0)
16
INSTR[5] | INSTR[0] | ARSrc Address Register | Command Parameter
0 | 0 | PC ({PC[H], PC[L]}) | %PC
1 | 0 | SP | %SP
SDW R2, 16(%SP)
*(ARSrc + Imm) = Rs (Rd as source)
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 75: Micro-Instructions Control: Store Data Byte with Offset 2 (SDW2) (10111)
Cycle # | Instruction | Explanation
0 | 0x08_00_40 | Write Imm to the Data Bus, write ARSrc to the Address Bus, and set TmpAR to read.
1 | 0x10_28_10 | Write TmpAR to the Address Bus, write Rs (Rd) to the Data Bus, and set Memory to read from the Data Bus.
2 | 0x00_00_80 | Advance PC.
75
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
SDW | Immediate (8-bit) |  | Immediate (8-bit) | Rs (Rd) | ARSrc[1] | OpCode=17 (and ARSrc[0] = 1)
17
INSTR[5] | INSTR[0] | ARSrc Address Register | Command Parameter
0 | 1 | DP | %DP
1 | 1 | BP | %BP
SDW R0, %BP, #0
*(ARSrc + Imm) = Rs (Rd as source)
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 76: Micro-Instructions Control: Address with Offset to Address 1 (MAA1) (11000)
Cycle # | Instruction | Explanation
0 | 0x08_00_40 | Write Imm to the Data Bus, ARSrc to the Address Bus, and set TmpAR to read.
1 | 0x10_00_00 | Write TmpAR to the Address Bus.
2 | 0x32_00_00 | Write TmpAR to the Address Bus, Address Bus Low register to the Data Bus, and set ARDest[L] to read from the Data Bus.
3 | 0x66_00_00 | Write Address Bus High Register to the Data Bus and set ARDest[H] to read from the Data Bus.
4 | 0x_00_00_80 | Advance PC.
76
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
MAA | Immediate (8-bit) |  | Immediate (8-bit) | ARDest | ARSrc[1] | OpCode=18 (and ARSrc[0] = 0)
18
MAA %SP, %SP, #-1
ARDest = ARSrc + Imm
INSTR[5] | INSTR[0] | ARSrc Address Register | Command Parameter
0 | 0 | PC ({PC[H], PC[L]}) | %PC
1 | 0 | SP | %SP
0-PC, 1-DP, 2-SP, 3-BP
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 77: Micro-Instructions Control: Address with Offset to Address 2 (MAA2) (11001)
Cycle # | Instruction | Explanation
0 | 0x08_00_40 | Write Imm to the Data Bus, ARSrc to the Address Bus, and set TmpAR to read.
1 | 0x10_00_00 | Write TmpAR to the Address Bus.
2 | 0x32_00_00 | Write TmpAR to the Address Bus, Address Bus Low register to the Data Bus, and set ARDest[L] to read from the Data Bus.
3 | 0x66_00_00 | Write Address Bus High Register to the Data Bus and set ARDest[H] to read from the Data Bus.
4 | 0x_00_00_80 | Advance PC.
77
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
MAA | Immediate (8-bit) |  | Immediate (8-bit) | ARDest | ARSrc[1] | OpCode=19 (and ARSrc[0] = 1)
19
MAA %DP, %BP, #-1
ARDest = ARSrc + Imm
INSTR[5] | INSTR[0] | ARSrc Address Register | Command Parameter
0 | 1 | DP | %DP
1 | 1 | BP | %BP
0-PC, 1-DP, 2-SP, 3-BP
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 78: Micro-Instructions Control: Move Address to General register (MAG) (11010)
Cycle # | Instruction | Explanation
0 | 0x00_00_00 | Write ARSrc to the Address Bus (special behavior due to opcode being MAG).
1 | 0x20_00_20 | Write Address Bus L/H Register to the Data Bus (L or H determined by the (AR) L/H instruction operand) and set Rd to read from the Data Bus.
2 | 0x00_00_80 | Advance PC.
78
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
MAG | XXXX |  | ARSrc | Rd | (AR) L/H | OpCode=1a
1A
MAG R3, %SP, L
Rd = ARSrc[L/H]
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 79: Micro-Instructions Control: Load Address register(LDA) (11011)
Cycle # | Instruction | Explanation
0 | 0x02_00_40 | Write Imm to the Data Bus and set ARDest[L/H] to read from the Data Bus.
1 | 0x00_00_80 | Advance PC.
79
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
LDA | Immediate (8-bit) |  |  | ARDest | (AR) L/H | OpCode=1b
1B
LDA %BP[L], #0x05
ARDest[L/H] = Imm
0-PC, 1-DP, 2-SP, 3-BP
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 80: Micro-Instructions Control: Move General to Address register (MGA) (11100)
Cycle # | Instruction | Explanation
0 | 0x02_00_10 | Write Rs1 to the Data Bus and set ARDest[L/H] to read from the Data Bus.
1 | 0x00_00_80 | Advance PC.
80
Type | 15 14 | 13 12 | 11 10 9 8 | 7 6 | 5 | 4 3 2 1 0
MGA | XX | Rs1 | X | ARDest | (AR) L/H | OpCode=1c
1C
MGA %SP[L], R2
ARDest[L/H] = Rs1
Bit | Operation
23 | Not Used
22 | AddressHorL
21 | AddressBusToDataBus
20 | TmpARWrite
19 | TmpARRead
18 | loadARHorL
17 | loadAR (formerly: Load Special Pointer)
16 | Stack Pointer Increment / Decrement (0: decrease / 1: increase)
15 | Stack Pointer Count
14 | SP Out (formerly: RAM Address Select (0: Address register / 1: Stack pointer))
13 | Use Rd as Source
12 | Lower Address Register Load
11 | Mem Write
10 | Mem Read
9 | PC Out
8 | PC Load
7 | PC advance
6 | Program Register H Write to Bus (parameter)
5 | Register File Input Enable
4 | Register File Output Enable
3 | Register File Output Select (parameter – 0 -> Rs1, 1 -> Rs2)
2 | ALU output enable
1 | ALU load register A
0 | ALU load register B

## Slide 81: (Data Bus  AR) Loading
We must be able to tell an AR to read from the Data Bus, and we must specify which byte (L or H) it should write the Data Bus’ data word into.
Inputs: L/H instruction operand (1 bit), ARDest instruction operand (2 bits), loadAR control signal, PC Load control signal, loadARHorL control signal, opcode
Output: {None (no AR reads), PC[Dummy H], PC[L], SP[H], SP[L], DP[H], DP[L], BP[H], BP[L]}
(Note: Can’t write to the actual PC H, can only write to the PC Dummy H from the data bus! Actual PC H only reads from the Dummy PC High!)
PC Load Branch | loadAR control signal | PC Load control signal | Opcode_MAA (active low) | loadARHorL control signal | L/H instruction operand | Output
Active (1) | X | X | X | X | X | PC[L] (and PC[H] = DHPC)
Inactive (0) | 1 | 1 | X | HorL | X | PC[HorL] (if L, PC[L] = data bus and PC[H] = DHPC)
Inactive (0) | 1 | 0 | MAA | HorL | X | ARDest[HorL]
Inactive (0) | 1 | 0 | Other Opcodes | X | L/H | ARDest[L/H]
Inactive (0) | 0 | X | X | X | X | None

## Slide 82: (Data Bus  AR) Loading (AR Data Bus Load Enable LUT)
The Data Bus  AR Loading combinational logic (explained in previous slide) is implemented as a (8 bit  8 bit) (256 byte) LUT in an EEPROM.
EEPROM Address Bit | Input
7 | PC Load Branch (ACTIVE LOW)
6 | loadAR (control signal)
5 | PC Load (control signal)
4 | loadARHorL (control signal)
3 | Opcode_MAA (ACTIVE LOW)
2 | (AR) L/H instruction operand
1 | ARDest[1]
0 | ARDest[0]
EEPROM Data Output Bit | Output
7 | BP[H] Load Enable (ACTIVE LOW)
6 | BP[L] Load Enable (ACTIVE LOW)
5 | SP[H] Load Enable (ACTIVE LOW)
4 | SP[L] Load Enable (ACTIVE LOW)
3 | DP[H] Load Enable (ACTIVE LOW)
2 | DP[L] Load Enable (ACTIVE LOW)
1 | DHPC Load Enable (ACTIVE LOW)
0 | PC[L] + PC[H] = DHPC Load Enable (ACTIVE LOW)

## Slide 83: 138 - 3-to-8 Line Decoder

## Slide 84: 161 - 4-Bit Binary Counter, Asynchronous Reset
Notes:
Parallel Load need to happen on invese clock
Count need to happen on [TBD – need timing diagram of the PC Advance]

## Slide 85: 175 - Quad D-Type Flip-Flop with Reset

## Slide 86: 245 - Octal D-Type Flip-Flop with Reset

## Slide 87: 273 - Octal D-Type Flip-Flop with Reset

## Slide 88: 547 - Octal 3−State Noninverting D Flip−Flop